## Slide 1: “Optical Measurements” Master Degree in Engineering Automation-, Electronics-, Physics-, Telecommunication- Engineering
<number>/57
LASER Sources: Principles of Operation prof. Cesare Svelto Politecnico di Milano
Notes: 07/29/26
<number>
Buongiorno a tutti,
sono Cesare Svelto
del Politecnico di Milano.
Questa mattina vi parlerò delle sorgenti laser in continua e delle pricipali misure per la loro caratterizzazione.
Descriveremo la struttura dei laser a stato solido e dei laser a semoconduttore (diodi laser)
per la caratterizzazione di sorgenti laser in continua e dei campioni ottici di frequenza.
La prima parte del mio intervento sarà seguita da una lezione del Prof. Elio Bava sui modelli descrittivi dell’instabilità di frequenza e sulle relative tecniche di misura.
Nella seconda metà della mia presentazione descriverò, dal punto di vista sperimentale, alcuni metodi ed esperienze di stabilizzazione e la realizzazione di campioni ottici di frequenza.

## Slide 2: Before it was DARK…
<number>/53
Sorgenti Laser: Principi di Funzionamento Caratteristiche e Applicazioni Cesare Svelto Politecnico di Milano
Notes: 07/29/26
<number>
Buongiorno a tutti,
sono Cesare Svelto
del Politecnico di Milano.
Questa mattina vi parlerò delle sorgenti laser in continua e delle pricipali misure per la loro caratterizzazione.
Descriveremo la struttura dei laser a stato solido e dei laser a semoconduttore (diodi laser)
per la caratterizzazione di sorgenti laser in continua e dei campioni ottici di frequenza.
La prima parte del mio intervento sarà seguita da una lezione del Prof. Elio Bava sui modelli descrittivi dell’instabilità di frequenza e sulle relative tecniche di misura.
Nella seconda metà della mia presentazione descriverò, dal punto di vista sperimentale, alcuni metodi ed esperienze di stabilizzazione e la realizzazione di campioni ottici di frequenza.

## Slide 3: … and now “we have THE LIGHT”!
<number>/53
Sorgenti Laser: Principi di Funzionamento Caratteristiche e Applicazioni Cesare Svelto Politecnico di Milano
Notes: 07/29/26
<number>
Buongiorno a tutti,
sono Cesare Svelto
del Politecnico di Milano.
Questa mattina vi parlerò delle sorgenti laser in continua e delle pricipali misure per la loro caratterizzazione.
Descriveremo la struttura dei laser a stato solido e dei laser a semoconduttore (diodi laser)
per la caratterizzazione di sorgenti laser in continua e dei campioni ottici di frequenza.
La prima parte del mio intervento sarà seguita da una lezione del Prof. Elio Bava sui modelli descrittivi dell’instabilità di frequenza e sulle relative tecniche di misura.
Nella seconda metà della mia presentazione descriverò, dal punto di vista sperimentale, alcuni metodi ed esperienze di stabilizzazione e la realizzazione di campioni ottici di frequenza.

## Slide 4: Summary (1)
<number>/57
Historical perspective, e.m. spectrum, dualism of light
Stimulated emission, optical amplification, optical resonators, LASER action
Pump methods and population inversion
Active media and LASER types
Gas LASERs (CO2 and He-Ne)
Solid-state LASERs with optical pumping (Nd:YAG) [DPSSL]
  side-pumped and end-pumped LASERs
Semiconductor LASERs (Laser Diodes) [LDs]
  LDs for pointing, optical reading, printers, …
  Single-Mode LDs for Optical Communications (DFB, DBR, VCSEL)
  Single-Mode narrow linewidth LASERS for precision measurements:
  Extended-Cavity Laser Diode (ECLD), Er:fiber and Er:bulk LASERs
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 5: Summary (2)
<number>/57
Pulsed LASERs (Q-switching and mode locking)
Examples of prevalent lasers, features, applications
Propagation and spatial profile measurements
  spot size
  divergence
Properties of laser beams
  Spatial and spectral properties
  Amplitude and frequency noise
Definition and measurement of optical power
Direct and coherent optical detection
Applications of LASERs and laser safety
Bibliography
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 6: Historical perspective and laser properties
<number>/57
LASER invented in 1960 (T. Maiman)
Light Amplification
by Stimulated Emission of Radiation
Starting from previous works on MASERs (1954) and the corresponding microwave oscillators, Research moved to the much higher optical frequencies where the energetic quantum phenomena are more evident
The LASER is a light source with excellent properties:
  monochromaticity, coherence (spatial and temporal), directionality, brightness ( energy density in space), polarization, time duration ( energy density in time)
Notes: 07/29/26
<number>
Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 7: The electro-magnetic spectrum
<number>/57
  millimeter waves (10mm-1mm)
  Far- and Medium- IR (1000m -2.5m)
  Near-IR (2.5-0.75m)
  VISible (750nm-380nm)
  UV (380nm-40nm)
  X-rays soft (40nm-1nm)
  X-rays hard (1nm-0.01nm)
   rays(10pm-0.01pm)
mm
IR
NIR
VIS
UV
X
 [nm]  [THz]
107 0.03
106 0.3
2500 120
750 400
380 790
40 7500
1 3105

LASERs working in CW or PULSED regime
Oscillators at “optical” frequencies ( f ~ 500 THz )
  f   with =c/ wavelength
(optical carrier stationary or modulated)
color  (nm)
red 750-620
orange 620-585
yellow 585-575
green 575-500
blue 500-445
indigo 445-425
violet 425-380
LIGHT
Notes: 07/29/26
<number>
Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 8: “Optical” wavelengths (LightWaves)
<number>/57
“LIGHTWAVES”
1mm
10nm
5 decades
Notes: 07/29/26
<number>
Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 9: Representations of light
<number>/57
WAVE ( wave theory )
  interference phenomena
  diffraction phenomena
PHOTON ( corpuscle theory)
  energy quantization E=h
  interaction radiation/matter
  (photon absorption/emission)
RAYS ( geometrical optics )
  analysis of optical systems: reflection/refraction
  most finely: Gaussian Optics
Notes: 07/29/26
<number>
Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 10: Absorption, spontaneous emission, stimulated emission
<number>/57
h =E2-E1
 = hc/(E2-E1)
In the process of stimulated emission,
an incident photon is “amplified”
producing two coherent photons (interaction of light with excited atoms)
2
1
E2
h
E1
absorption
ATTENUATOR
2
1
E2
h
E1
stimulated emission
h
h
AMPLIFIER
2
1
E2
h
E1
spontaneous emission
EMITTER
sp
U(EL)
L(EL)
( ( all effects are due to different energy states in the atom ) )
Notes: 07/29/26
<number>

## Slide 11: Optical amplification (coherent)
<number>/57
Spontaneous Emission: (incoherent emission)
energy is emitted with frequency not exactly predetermined and with random phase and direction
Stimulated Emission: (coherent emission)
energy is emitted with the same frequency, phase, direction
ENERGY LEVELS
upper: E2
lower: E1
atoms
ions in glass or crystal
molecules (also vibrational)
bands (semiconductors)
Notes: 07/29/26
<number>

## Slide 12: Population inversion
<number>/57
N2 < N1
ATTENUATOR
At thermodynamic equilibrium, with E2 > E1 , it is N2 < N1
N = [1/cm3] = = [atoms/cm3]
N = (N2 - N1) is called POPULATION INVERSION
If N2 = N1 (which holds also for N2=N1=0) the medium is "transparent" to the specific  and  considered
N2 > N1
AMPLIFIER
“disequilibrium” with ‘excited’ atoms
Notes: 07/29/26
<number>

## Slide 13: Elements of a LASER oscillator
<number>/57
1. Active MEDIUM atoms/ions/molecules with “suitable” energy levels
1. + 2.  device with GAIN
amplifier
3.  way for optical feedback
feedback (+)
(LASER action)
G
A I N
LOSSES
(laser oscillation)
OSCILLATOR
2. PUMP mechanism
energy transfer to provide for “population inversion”, by “exciting” the active medium and obtain optical gain
3. Optical RESONATOR
system for e.m. radiation confinement
Notes: 07/29/26
<number>

## Slide 14: Optical amplification (??? 2 levels)
<number>/57
Even by supplying energy to the system, it is impossible to achieve (“net”) amplification by a system with 2 energy levels
When N1=N0=N/2 any additional pump energy gives the same probability of transition 01 and 10
Two-level system
condition for amplification: N1  N0 (impossible)
0
1
pump
radiative transition
ground level
“It is not sufficient to promote N/2 atoms in the upper level” (and it is not possible promoting more than N/2)
UEL
LEL
Notes: 07/29/26
<number>

## Slide 15: Optical amplification (3 levels)
<number>/57
In order to obtain amplification we must supply
energy to a system with more than 2 levels
POPULATION INVERSION
N1 - N0 > 0
Three-level system
working condition
21 << 10
condition for amplification: N1  N0 (not simple)
“We must promote N/2+n atoms in the upper level”
because lev. 0
must be emptied
0
2
1
pump
non-radiative transition
radiative transition (LASER effect)
ground level
UEL
LEL
Notes: 07/29/26
<number>

## Slide 16: Example of 3-level LASER (Ruby)
<number>/57
Ruby: Al2O3 (aluminum oxide: -alumina, or corundum) where some of the Al3+ ions are substituted by Cr3+
IN GENERAL: The procedure of doping tiny amounts of the metals chromium (Cr), neodymium (Nd), erbium (Er), thulium (Tm), ytterbium (Yb), and a very few others, into transparent crystals, ceramics, or glasses provides the active medium for solid-state lasers.
Cr2O3 (by-weight) substitution for Al2O3 in Natural Ruby is 1% Synthetic Ruby is 0.05%
P,visible(BLUE-GREEN)= 0.42-0.55 m < L = 0.69 m
Notes: 07/29/26
<number>

## Slide 17: Optical amplification (4 levels)
<number>/57
condition for amplification: N2  0 (simple)
Most efficient system: 4 LEVELS
working condition
32 , 10 << 21
Four-level system
0
3
2
pump
non-radiative transition
radiative transition (LASER effect)
non-radiative transition
1
ground level
“It is sufficient to promote any n atoms in the upper level”
because lev. 1
is already empty
UEL
LEL
Notes: 07/29/26
<number>

## Slide 18: Example of a 4-level LASER (Nd:YAG)
<number>/57
YAG: Yttrium Aluminum Garnet (Y2Al5O12) with some Y3+ atoms/ions substituted by Nd3+ (1%)
3
2
1
0
Notes: 07/29/26
<number>

## Slide 19: Nd:YAG LASER and “Quantum defect”
<number>/57
Energy EP of the pump photon must be higher than energy EL of laser photon ( hP > hL )
P= 0.8 m < L = 1.06 m
EP= hP = hc/P  2.46×10-19 J
EL = hL = hc/L  1.87×10-19 J E = 5,92×10-20 J E / EP = 24 %
this energy gets “lost” and is provided to the atoms of the crystal in the form of reticle vibrations (phononic excitation) turning into temperature rise of the active medium
1
2
3
0
Notes: 07/29/26
<number>

## Slide 20: Optical amplification (quasi-3-levels)
<number>/57
condition for amplification: N2  0 (not so simple)
Intermediate behavior: 4-3 LEVELS
working condition
32 , 10 << 21
Quasi-3-level system
0
3
2
pump
non-radiative transition
radiative transition (LASER effect)
non-radiative transition
1
ground level
“We must promote n > m atoms in the upper level”
because lev. 1
is partly (m) full
UEL
LEL
Notes: 07/29/26
<number>

## Slide 21: Yb:YAG LASER, low Quantum defect
<number>/57
Energy EP of pump photon must be higher than energy EL of laser photon ( hP > hL )
P= 0.94 m < L = 1.03 m
EP= hP = hc/P  2.12×10-19 J
EL = hL = hc/L  1.93×10-19 J E = 1,85×10-20 J E / EP = 8.7 %
this energy gets “lost” and is provided to the atoms of the crystal in the form of reticle vibrations (phononic excitation) turning into temperature rise of the active medium
Notes: 07/29/26
<number>

## Slide 22: Er:glass LASER “quasi-three-level”
<number>/53
P= 0.98 m < L = 1.55 m
Optical gain and emitted wavelengths from 1480 nm to 1620 nm: 3th transmission window of optical fibers (loss <0.2dB/km).
A complicated balancing mechanism between gain and losses (depending also on the pump rate) allows broad wavelength emission spectrum
Notes: 07/29/26
<number>

## Slide 23: Summary of “LASER level” schemes
<number>/57
3-level 4-level quasi-three-level
Notes: 07/29/26
<number>

## Slide 24: Types of pumping mechanisms
<number>/57
ELECTRICAL DISCHARGE ( gases )
  the energy of the electrical discharge excites, via collisions (kinetic energy transfer) the atoms/ions in the active medium
OPTICAL ( crystals, gases, liquids )
  the pump photons excite atoms/ions
ELECTRICAL CURRENT ( semiconductor )
  the energy of the electrical current in the semiconductor (energy of electron-hole recombination) provides emitted radiation
Notes: 07/29/26
<number>

## Slide 25: Review of energy levels, pumping, and population inversion (4 lev.)
<number>/57
3
2
1
0
pumping
rapid decay
LASER action
rapid decay
N3  0  N1
21 >> 32 , 10
Population inversion:
N2>N10
The active medium can amplify radiation at laser
 laser
long-lived
state
Notes: 07/29/26
<number>

## Slide 26: Optical gain in an active medium
<number>/57
Amplification by unit of length (dz) in the active medium
emission cross section (cm2 or pm2)
optical intensity (W/cm2)
N population inversion (cm-3)
For an active medium of length l:
logarithmic gain g (cm-1)
single-pass optical gain
I(0)
I(l )
l
I I+dI
dz
Notes: 07/29/26
<number>

## Slide 27: Elements of a LASER oscillator (bis)
<number>/57
1. Active MEDIUM atoms/ions/molecules with “suitable” energy levels
1. + 2.  device with GAIN
amplifier
3.  way for optical feedback
feedback (+)
(LASER action)
G A I N
LOSSES
(laser oscillation)
OSCILLATOR
2. PUMP mechanism
energy transfer to provide for “population inversion”, by “exciting” the active medium and obtain optical gain
3. Optical RESONATOR
system for e.m. radiation confinement
SEEN
Notes: 07/29/26
<number>

## Slide 28: Fabry–Perot optical resonators
<number>/57
L
Optical Resonator
R1
mirror
R2
mirror
resonance conditions
resonant
length
L = m   / 2
resonant frequencies
 = m  c / 2L
free-spectral range
FSR = c / 2L
the integer m, is the order of the resonant mode and tells us how many  there are in a round-trip (2L)
or on which order of the FSR is the frequency 
In order to maintain the same phase of the e.m. field for the wave traveling back and forth between the mirrors, the round-trip path must be an integer multiple of the wavelength: 2L = m  
resonant wavelengths  = 2L/m  1/m
Notes: 07/29/26
<number>

## Slide 29: Properties of Fabry-Perot resonator
<number>/57
Cavity lifetime
 c = L / c
 losses (logarithmic) per pass… see later
Cavity linewidth (FWHM)
 c = 1 / 2 c = c / 2L
Quality factor
(resonance factor)
Q = (c / )-1=  / c
Q = (/FSR)F
Q = m  F
( “best mirrors” provided F=600 000, hence R=99.999 5%=1-T-A “indirect meas.” )
L
Pin
Pout
Finesse F = FSR /  c
F = (R 1R 2)1/4 / 1- (R 1R 2)1/2
F = R1/2/ (1- R) with R=(R1R2)1/2
R1[=99.9%]
mirror
R2[=99.9%]
mirror
[F  3140]
R1
R2
c/2L
T = Pout / Pin
m
m+1
F = ?
constant  F ;  c
Notes: 07/29/26
<number>

## Slide 30: Transmission of the Fabry-Perot
<number>/57
c/2L
T = Pout / Pin
m
m+1
Airy spectral profile
for R=R1=R2
 = (2 2L/) =(ks)=
= (2 2L/c)
cos( )=+1
  = n(2)
cos( )= -1
  = n(2)+
Linear axis in  or  (not in )
round trip
Notes: 07/29/26
<number>

## Slide 31: Optical gain in an active medium (bis)
<number>/57
Amplification, per unit length, in the active medium
For an active medium of length l:
single-pass optical gain
For each pass in the active medium the optical beam experiences an un optical gain G in intensity/power
Let’s find the value of critical gain (and critical inversion) allowing the start of laser oscillation in an active medium undergoing positive feedback
I I+dI
dz
Notes: 07/29/26
<number>

## Slide 32: Threshold condition for laser action
<number>/57
The round-trip (double-pass) gain must equal the losses within the resonator (mirrors reflectivity, surfaces and materials crossed by the beam, diffraction).
Considering (ideal case) only the partial reflectivity of the mirrors (R1, R2 < 1)
I0
GI0
R2GI0
GR2GI0
in a round-trip path it must be R1GR2GI0 = I0  G 2=1/(R1R2)
exp[2 (N2-N1)l] = 1/(R1R2)   (N2-N1)l =(1/2)[-ln(R1) -ln(R2)]=
mirror 1
R1
mirror 2
R2
active medium
G
l
R1GR2GI0
Notes: 07/29/26
<number>

## Slide 33: Critical inversion, threshold power and slope efficiency in a LASER
<number>/57
with
single-pass log. losses  (1) Any other additional loss in addition to R1 and R2 should be incorporated into 
saturation
slope efficiency
Pth
Pl
Pp
INPUT-OUTPUT
PLOT
 =(1/2)[-ln(R1) -ln(R2)]= =-ln(R) logarithmic losses
gain = losses (N2-N1)l = threshold)
slope
Notes: 07/29/26
<number>

## Slide 34: Active medium, pumping, population inversion, laser action, optical feedback, laser oscillation
<number>/57
( Energy Level 3 )
Notes: 07/29/26
<number>

## Slide 35: Elements of a LASER oscillator (ter)
<number>/57
1. Active MEDIUM
atoms/ions/molecules: energy levels
2. PUMP mechanism [and laser threshold]
Energy transfer “exciting” the Active Medium achiving a “population inversion” in order to obtain an optical gain
3. Optical RESONATOR
system for e.m. radiation confinement
… now let’s see the STRUCTURE of a LASER …
SEEN
Notes: 07/29/26
<number>

## Slide 36: Structure of a LASER oscillator
R1=100 %
mirror
Optical Resonator (3.)
R2=90 %
mirror
<number>/57
THRESHOLD Pth = Ppump,min for Plaser>0
SLOPE EFFICIENCY
 = Plaser / Ppump
Colors are only for visual purpose …
Pump (2.)
Ppump
Active Medium (1.)
laser beam
Plaser
Notes: 07/29/26
<number>

## Slide 37: LASER Types (classification criteria)
<number>/57
1. Physical state and properties of the active medium:
  gas LASERs (in a gas)
  colorant LASERs (in a liquid)
  solid-state LASERs (in solid with crystal or amorphous host)
  semiconductor LASERs (in a solid semiconductor; Laser Diode)
3. Operating regime
  CONTINUOUS WAWE (CW) LASERs multi-mode, single-mode (long./trasv.), single-frequency
  PULSED LASERs pulsed free-running, Q-switching, mode-locking
2. Emission wavelength
  LASERs in the IR, VIS, UV, and X-ray
Notes: 07/29/26
<number>
I materiali otticamente attivi, e quindi i tipi di laser realizzabili, possono essere suddivisi in diverse categorie a seconda dello stato fisico e delle proprietà del materiale attivo, in base alla lunghezza d'onda di emissione o secondo il regime di funzionamento.

## Slide 38: Gas LASERs (electrical discharge pump)
<number>/57
Sealed tube
( He-Ne )
( 10 : 1 )
The electrical discharge excites (by electron-atom impact) the He atoms that transfer their excitation energy (resonant energy-transfer) to the Ne atoms finally providing LASER action in the RED
Flow tube
( CO2 )
 = 10.6 m (IR) P  kW
 = 632.8 m (VIS) P  mW
Notes: 07/29/26
<number>

## Slide 39: Solid-state LASERs (side-pumping)
<number>/57
Active Medium
Rlaser=100 %
mirorr
LASER output
Rlaser=70 %
output mirror
(e.g.Nd:YAG)
(=1.064 m)
lamp optical pumping
Pump lamp (e.g. Xe o Kr)
reflecting wall
reflecting wall
Notes: 07/29/26
<number>

## Slide 40: Solid-state LASERs (end-pumping) (specific example with Nd:YAG)
<number>/57
Active Medium
Rlaser=100 %
Tpump>90 %
mirror
Rlaser=90 %
output
mirror
LASER output
Nd:YAG
=1.064 m
Yttrium Aluminum Garnet
YAG  Y3Al5O12
yttrium oxide + alumina
( Y2O3 + Al2O3 )
Nd atoms substitute
Y atoms by 1% in the crystal host
Pump diode
coupling optical system
AlGaAs
=808 nm
Notes: 07/29/26
<number>

## Slide 41: Properties of the active medium Nd:YAG: 1%-atomic =0.725%-weight)
<number>/57
(4 level laser)
(NIR)
(a few ppm)
(very high)
(very long  ¼ ms)
(high)
(modest thermal lensing)
Example (optical power for ½ Nd atoms in 1 cm3 lasing in 1 second):
E=h=6.610-34300 1012=210-19 J
P = (½N)(1 cm3)E/t  10 W
= N
(stress/strain: “elasticity”)
Notes: 07/29/26
<number>

## Slide 42: Light absorption in Nd:YAG
<number>/57
The absorption spectrum provides a strong absorption peak at 808 nm
Pp,out = Pp,l = Pp,0 exp (-l)
logarithmic scale
 (cm-1)
Lambert
Beer
LAW
l=0.5 cm ; =10 cm-1
Pp,out = Pp,0 exp (-5) PABS=99.3%Pp,0 = =Pp,0 [1-exp (-5)] l=0.5 cm ; =2 cm-1
Pp,out = Pp,0 exp (-1) PABS=63%Pp,0 = =Pp,0 [1-exp (-1)]
1/5 in  is not 1/5 in PABS
Notes: 07/29/26
<number>

## Slide 43: Optical pumping: lamp vs diode
<number>/57
Comparison of emission spectra (lamps/LDs) for Nd:YAG pumping
Fig. 6.6 pag. 207
The spectral efficiency of diode pumping [ ] ( ~ 10 nm)
is much higher than for lamp pumping [ ] ( ~ 200500 nm)
Pump energy not usefully absorbed will produce
excess heat (thermal lensing and also irreversible damages)
Notes: 07/29/26
<number>

## Slide 44: Pump geometry: lamp vs diode
<number>/57
Fig. 6.1 pag. 204
Fig. 6.2 pag. 205
Fig. 6.3a pag. 205
Transverse optical pumping
with one, two and more lamps
Fig. 6.15 pag. 220
Fig. 6.16 pag. 220
Transverse LD pumping
for an Nd:YAG laser rod
Pump spatial distribution in the active medium
Pump: 150 W LASER: 62 W CW TEM00
Notes: 07/29/26
<number>

## Slide 45: Longitudinal Modes and Gain Bandwidth
<number>/57
2/2L
long. modes of the resonator
c/2L
frequency distance
(resonant wavelengths)
G

gain profile of the active medium BW=GFWHM
All longitudinal modes with “enough gain” do oscillate simultaneously (MLM). Typically the LMs closer to the peak of the gain profile will oscillate at the same time.
the LASER is not oscillating on a single-mode (-frequency)
distribution of energy levels
M L M oscillation
G or T
FSR
Notes: 07/29/26
<number>

## Slide 46: SLM selection
<number>/57
G or T

Optical Filter (band-pass) with F< c/2L
gain profile of the active medium
c/2L
modes of the resonator
1 laser mode Single-Longitudinal-Mode
example: “high-Finesse” Fabry-Perot etalon ( and “short enough” to have FSR>GFWHM )
S L M oscillation
Notes: 07/29/26
<number>

## Slide 47: Single-mode semiconductor LASERs
<number>/57
Distributed Feed-Back (DFB)
VCSEL
Distributed Bragg Reflector (DBR)
SLM due to “spectral filtering” of the monolithic optical resonator
FP less used
Wavelength selective “MIRROR”
Notes: 07/29/26
<number>

## Slide 48: 1.5 m narrow-linewidth LASERs
<number>/57
Extended Cavity LD (ECLD)
Er fiber LASER
Bulk Er-Yb LASER

Notes: 07/29/26
<number>

## Slide 49: Pulsed LASERs : Q-switching
<number>/57
mechanical
on/off e.g. 1 Hz
(giant pulse)
electro-optic
1 kHz “high gain”
acousto-optic
10-100 kHz “low gain”
All the pump energy accumulated in the active medium is released, in a short time, when the resonator is “aligned” (high Q condition)
With low Q the population inversion can grow higher, achieving N much higher than Nth
Time interval TREP between pulses: depends on the switch
Pulse duration p: depends on active medium (10 ns)
duty cycle (p/TREP) is low  peak power is high (MW)
Notes: 07/29/26
<number>

## Slide 50: Pulsed LASERs: mode-locking
<number>/57
phase-locked longitudinal modes
TREP = 2L/c (round trip)
fREP=1/TREP (100 MHz 10 GHz)
p = 1/Blaser (10 ps  100 fs)
Ppeak very high (up to >GW)
1.5 m 1.5 cm
fREP=c/2L=1FSR
fREP=2FSR
fREP=3FSR
TREP
TREP
Notes: 07/29/26
<number>

## Slide 51: Femtosecond LASER (mode locking)
<number>/57
TREP = Lf /c (round trip)
fREP=1/TREP (250 MHz)
Lf = cTREP= c / f REP= 1.2 m
p = 1/Blaser (<90 fs e.g. 80 fs)
Pave = 10 mW  400 mW (e.g. 200 mW)
Pp=Pave [TREP/p]=200 mW [4 ns/80fs]= =100 kW (with Pelet=100 W)
Notes: 07/29/26
<number>

## Slide 52: Applications of femtosecond LASERs
<number>/57
Notes: 07/29/26
<number>

## Slide 53: Properties of the Nd:YAG LASER
<number>/57
Energy levels of the ion Nd3+ in YAG crystal ( Y3Al5O12 )
Doping in the order of 1-2 % (Nd3+ substituting Y3+)
Gain bandwidth  = 125 GHz (0.4 nm) [40 in glass]
Slope efficiency 3÷5 % (lamps) and >20 % (diodes)
pump
730 nm
808 nm
laser transition at 1.064 m
 = 0.23 ms
  100 ns
Energy >> kT
  100 ns
4I9/2
4I11/2
4F3/2
4F5/2
946 nm
Notes: 07/29/26
<number>

## Slide 54: Pulsed Nd:YAG LASER
<number>/57
  1 m and   300 THz
Operating in a mode-locking regime
YAG  0.4 nm e glass  40YAG  16 nm

Er:glass (fiber) =1.55 m  =80 fs   =12.5 THz  =100 nm
Notes: 07/29/26
<number>

## Slide 55: Main properties of typical LASERs
<number>/57

Pp=10 9 W in mode-locking
10-3- 1
33
diode-pumped
10000
0.1
Laser

(

m)
P
(W)
Dimension
(m)
Efficiency
(%)
Cost
(
€
)
He
-
Ne
0.632
(rosso)
10
-
3
-
10
-
2
0.1
-
1
0.1
100
-
2000
Nd:YAG
1.064
200 (CW)
10
7
(peak)
1
1
-
10
50000
CO
2
10
10
4
(CW)
10
7
(peak)
1
10
-
20
50000
Semiconductor
0.45
-
1.6
1
10
-
3
50
10
-
10000
Notes: 07/29/26
<number>

## Slide 56: Example of “typical” LASER: He-Ne
<number>/57
Notes: 07/29/26
<number>

## Slide 57: Example of “typical” LASER: Nd:YAG 2
<number>/57
An ultra bright pointer is now on the market [class IIIA] (5 mW at the green 532 nm wavelength): an intracavity frequency-doubled Nd:YVO4 laser with blocked IR.
Notes: 07/29/26
<number>