## Slide 1: Politecnico di Milano Optical Measurements ”LASER INTERFEROMETRY”
Ing. Enrico Maria Randone, Ph.D.
Dipartimento di Elettronica - Università di Pavia
Tel. 0382 98 5224
e-mail: enrico.randone@unipv.it
It is acknowledged the origin of some figures, photos and texts
as didactic material originally produced by Prof. Silvano Donati (Università di Pavia)
and/or Dr. Eng. Guido Giuliani (Università di Pavia)

## Slide 2: Read-out Configurations of Interferometry (I)
EXTERNAL configuration (what we have seen until now):
It’s the more common scheme
The interferometer is external to the laser cavity
Displacement reading is obtained from the optical phase  = 2ks through the INTENSITY modulation: I = I0 cos(2ks)
PD
LASER
Mr
Mm
s

## Slide 3: Read-out Configurations of Interferometry (II)
INTERNAL configuration: Ring Laser Gyro(scope) (RLG)
The laser emits on two different longitudinal modes: Mode 1 (@ frequency 1) is sustained from the reference cavity (Mb-Mr), and Mode 2 (@ frequency 2) is sustained from the measuring cavity (Mb-Mm). If Mm moves, the frequency of Mode 2 changes
The photodiode detects the beating of modes 1 & 2, and generates a signal at the (electrical) frequency Δ ≈ (c/2L) Δs / (λ/2) and I = I0 cos(2πΔ t). The displacement reading is obtained from a FREQUENCY measurement
Maximum displacement is given by Δsmax= λ/2, but this scheme is VERY SENSITIVE: Rf = Δ / Δs = c(Lλ)-1 = 2.4MHz/nm, for typical He-Ne tube with L=20cm
PD
LASER
Mr
Mm
Δs
Mb
L

## Slide 4: Self-Mixing (or Injection) Configuration: Principle (I)
In this scheme we start from the unperturbed lasing field E0, a fraction of which (Er) propagates back-and-forth in the external cavity and is allowed to RE-ENTER the laser cavity
In the laser cavity Er adds as a vector to E0 and this is exactly what happens in a COHERENT SCHEME OF DETECTION: we still work at the QUANTUM LIMIT of detection
LASER
E0
Mm
s(t)
Er
S0
PD
Iph

## Slide 5: Self-Mixing (or Injection) Configuration: Principle (II)
φ
E0
 Er = αEreiφ
AM ≈ cos φ
FM ≈ sIn φ
φ = 2ks = 2k [ S0 + s(t) ], con k = 2π / λ
As a consequence of beating of Er and E0, the laser emission shows a modulation in frequency (FM) and amplitude (AM), strictly related to the phase shift φ = 2ks, and this fact explains the name of “SELF-MIXING”
Iph = I0 (1 + mAM) cos[(1 + mFM)ωt], con mAM = A cos(2ks) e mFM = B sin(2ks)
Two signals in quadrature  displacement S0 + s(t) can be obtained without any ambiguity!
LASER
E0
Sm
s(t)
Er
S0
PD
Iph

## Slide 6: Self-Mixing Interferometry: He-Ne Zeeman Scheme (I)
Perpendicular Zeeman Effect: the laser emits on two modes. The frequency difference of them is in the order of 1 - 2 = 100 kHz, and they are linearly and orthogonally polarized
One mode (1) is forced to remain in the laser cavity. The other one (2) can propagate back-and-forth in the external cavity and is then back-injected in the He-Ne laser: as a consequence, 2 now shows amplitude and frequency modulation that depends on the optical phase shift 2ks(t)
The target is a loud speaker: diffusing target  speckle pattern!!!
B
P1
P
45°
Magnetic field B is PERPENDICULAR
TO THE He-Ne TUBE
P
P1
Magnet
Magnet
He-Ne
PD
Integr.
Integr.
Freq.
Demod
Amp.
Demod
Derivat.
Derivat.
A
A
v(t)
s(t)
s(t)
Loudspeaker
Somm.
RMS.
sin(2ks)
cos(2ks)

## Slide 7: Self-Mixing Interferometry: He-Ne Zeeman Scheme (II)
On the PD 1 and 2 beat and AM and FM are downconverted to an electrical carrier at frequency 1 - 2 and the resulting photocurrent is: Iph = I0 (1 + mAM) cos[2π(1 - 2)t + mFM]
The processing of Iph is fully analog, as we use amplifiers, integrators, and derivative blocks
WHAT IS THE REAL ADVANTAGE OF THE ANALOG PROCESSING?
B
P1
P
45°
Magnetic field B is PERPENDICULAR
TO THE He-Ne TUBE
P
P1
Magnet
Magnet
He-Ne
PD
Integr.
Integr.
Freq.
Demod
Amp.
Demod
Derivat.
Derivat.
A
A
v(t)
s(t)
s(t)
Loudspeaker
Somm.
RMS.
sin(2ks)
cos(2ks)

## Slide 8: Self-Mixing Interferometry: He-Ne Zeeman Scheme (III)
Experimental waveforms:
THERE IS NO AMBIGUITY ON THE SIGN OF THE LOUDSPEAKER DISPLACEMENT AS AM AND FM SIGNALS ARE IN QUADRATURE!
s(t) as given by the analog
processing
Signals in PRESENCE
of Self-Mixing
Signals in ABSENCE
of Self-Mixing
s(t)
sin(2ks)
cos(2ks)
Iph
v(t) as given by the analog
processing

## Slide 9: Self-Mixing Interferometry with Laser Diode (LD) (I)
… It is not possible to force a single longitudinal mode LD to work on two orthogonal modes by means of the Zeeman effect 
… The phase noise (or the laser linewidth) is too high and the FM signal CANNOT BE EXTRACTED, even with the aid of a frequency stabilized external oscillator 
 An ambiguity can arise in the evaluation of the sign of the interferometric phase 2ks = 2k [ S0 + s(t) ] 
: 5.6 - 9 mm
LD
Monitor
PD
S0
Mm
s(t)
Variable
Attenuator
The LD is a very compact, relatively cheap, very efficient laser source, and it usually cames with a monitor PD 
BUT…
Focusing
Lens

## Slide 10: Self-Mixing Interferometry with Laser Diode (LD) (II)
Lang & Kobayashi equations: laser source and optical injection
Laser Cavity
External Cavity (S0)
ξ is called the back-injection parameter
τ = 2S0/c is the round-trip-time in the
external cavity
ω0τ = 2kS0
Iph = I0 [ 1 + mF(2ks)] … (only the AM can be easily processed!)
m is the index of modulation
F is a periodic function of the optical phase 2ks, with period 2π, and -1 ≤ F(2ks) ≤ 1

## Slide 11: Self-Mixing Interferometry with Laser Diode (LD) (III)
If F(2ks) has the behavior of a cosine function, cos(2ks), an usual processing can extract s, but the problem of the ambiguity remains…
The behavior of F(2ks) depends on trough the C parameter:
F(2ks) depends on:
LASER parameters
Target distance
Target reflectivity

## Slide 12: Self-Mixing Interferometry with Laser Diode (LD) (IV)
If F(2ks) has the behavior of a cosine function, cos(2ks), an usual processing can extract s, but the problem of the ambiguity remains…
The behavior of F(2ks) depends on trough the C parameter:
 | He-Ne | LD
Linewidth Enhancement Factor  | 0 | 1-6
Rl | 95%-99% | 30%
LLASER | 10-100 cm | 200-400 m

## Slide 13: Self-Mixing Interferometry with Laser Diode (LD) (V)
F(2ks)
F(2ks)
F(2ks)
F(2ks)
C = 0.01
C = 0.5
C = 1
C = 3
Self-Mixing regimes of operation as a function of the C parameter:
0 < C ≤ 0.1: VERY WEAK retro-injection
0.1 < C < 1: WEAK retro-injection
1 ≤ C < 4.6: MODERATE retro-injection
C > 4.6 : STRONG retro-injection

## Slide 14: Self-Mixing Interferometry with Laser Diode (LD) (VI)
Self-Mixing regimes of operation as a function of the C parameter:
0 < C ≤ 0.1: VERY WEAK retro-injection
0.1 < C < 1: WEAK retro-injection
1 ≤ C < 4.6: MODERATE retro-injection
C > 4.6 : STRONG retro-injection
F(2ks)
F(2ks)
F(2ks)
F(2ks)
C = 0.01
C = 0.5
C = 1
C = 3

## Slide 15: Self-Mixing Interferometry with Laser Diode (LD) (VII)
Experimental self-mixing signals for different values of the C parameter
C=0.01
C=0.7
C=3
Target Displacement
Each jump corresponds to an interferometric fringe
and to a target displacement of λ/2

## Slide 16: Self-Mixing Interferometry with Laser Diode (LD) (VIII)
When using an LD, moderate regime (C>1) of operation is easily achieved with a cooperative target, but also on a diffusive target!
Thanks to the saw-tooth shape of the self-mixing signal, the problem of the ambiguity is easily overcome 
C = 2.5
1.25 m
UP / DOWN
COUNTER

## Slide 17: Self-Mixing Interferometry with Laser Diode (LD) (IX)
Block diagram for a digital (fringes counting) processing scheme:
Waveforms:
Performance
  resolution: /2 = 335 nm (visible and cheap LD @ 670 nm)
  maximum target velocity: 0.335 m/s (if we use a bandwidth B = 1MHz)
  accuracy: 10-4 (LD FP); 10-5-10-6 (DFB LASER with temperature control @ 0.05 °C)
Trans-Z
Amplifier
Up
Signal
Derivative
(HP Filter)
Polarity
Discrimination
Up-Down
Counter
Display
Down
Self-Mixing
Signal
Derivative
100 s/div
0.2 s/div
300 ns

## Slide 18: Self-Mixing Interferometry Pros and Cons
Pros:
Simple, compact, and inexpensive
The signal is generated inside the laser cavity, and is thus detectable EVERYWHERE IN THE SYSTEM, EVEN ON THE TARGET
The scheme works well also on diffusive target
Alignment of the laser and the target is not critical as in the Michelson interferometer
Good bandwidth (in the order of MHz)
Performance are close to those of classical interferometer for both vibrometer and displacement measuring interferometer
Cons:
When a LD is used, the linewidth stability is poorer than the one of an He-Ne LASER
DL need to be controlled in temperature to avoid wavelength drifts or mode-hopping
Biasing current of LDs must be controlled, because the emitted optical frequency is also current-dependent

## Slide 19: Self-Mixing Interferometry with LD: what happens if the target is at rest? (I)
If the target is at rest, is it possible to measure the absolute distance S0?
2ks = 2k [ S0 + s(t) ] = 2kS0 = costant…
In a LD the wavelength of emission depends on the value of the biasing current…
Even more important: one of the strongest pros of LD is the possibility of obtaining a modulated optical power (and frequency) by direct modulation of the bias current…
Can we or we can not ???
LD
Monitor
PD
S0
Sm
s(t)
Variable
Attenuator
Focusing
Lens
Iph

## Slide 20: Self-Mixing Interferometry with LD: what happens if the target is at rest? (II)
λ(Ibias) is of the kind: λ = λ0 + ΔIbias(t)
As a consequence, a modulation of the bias current ΔIbias gives:
ϕ = 2kS0 = S0  Δϕ(t) = - Δλ(t)S0
If Δλ(t) is sufficiently large and a periodic function of time, fringes will develop in the Self-Mixing signal for each phase variation equal to 2π, as induced by the wavelength variation even with a steady target (S0=const.)
TA-DAH!!! Mission of measuring absolute distance S0 is accomplished! 
What is the achievable resolution ΔS0 of this measurement?
∂λ
∂I
4π
λ
4π
λ02
LD
Monitor
PD
S0
Sm
s(t)
Variable
Attenuator
Focusing
Lens
Iph