## Slide 1: “Optical Measurements” Master Degree in Engineering Automation-, Electronics-, Physics-, Telecommunication- Engineering
<number>/38
Alignment/Pointing and Dimensional Measurements Prof. Cesare Svelto Politecnico di Milano
Some pictures are taken from the Book “Electro-Optical Instrumentation: Sensing and Measuring with Lasers” by Prof. Silvano Donati
Notes: 07/29/26
<number>
Buongiorno a tutti,
sono Cesare Svelto
del Politecnico di Milano.
Questa mattina vi parlerò delle sorgenti laser in continua e delle pricipali misure per la loro caratterizzazione.
Descriveremo la struttura dei laser a stato solido e dei laser a semoconduttore (diodi laser)
per la caratterizzazione di sorgenti laser in continua e dei campioni ottici di frequenza.
La prima parte del mio intervento sarà seguita da una lezione del Prof. Elio Bava sui modelli descrittivi dell’instabilità di frequenza e sulle relative tecniche di misura.
Nella seconda metà della mia presentazione descriverò, dal punto di vista sperimentale, alcuni metodi ed esperienze di stabilizzazione e la realizzazione di campioni ottici di frequenza.

## Slide 2: Summary
<number>/38
Propagation and transformation (focusing, widening-and-collimation) of gaussian beams
Position sensitive detectors of laser beam - 4-quadrants photodiodes - PSD (Position Sensitive Detector) - reticle detectors
Laser level
Wire diameter measurement
Optical measurement of particulate dimensions
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 3: Laser alignment
<number>/38
One property of laser sources is the possibility of keeping the optical bem well collimated (slightly divergent and hence with “constant spot size" during propagation)
The divergence limit posed by diffraction theory (TEM00) is “easy to meet”: e.g. for a red He-Ne LASER (633 nm). Visible light is useful for alignment in a specific direction ("filo a piombo or lead-line" not only vertical)
We must minimize the laser spot dimension on the whole working region (range z*) and to this aim we must design an optimal value of the beam waist (w0) in the center of the range: for this purpose we use a telescope to “widen the spot size to the desired dimension"
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 4: Laser alignment in constructions
<number>/38
Typical instrument for laser alignment and its use in the construction of gas pipeline (LaserLight AG, Munich)
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 5: Propagation of a laser Gaussian beam
<number>/38
Divergence of the laser spot (free space)
Output beam from a laser (e.g. He-Ne) with plane-spherical cavity
ROC
beam waist in the plane-spherical resonator
it must be LROC
r = at z=0 and at z= (plane wave) minimum rMIN=2zR at z=zR
Curvature Radius of the wave front
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 6: Propagation trough a lens
<number>/38
f
Transformation of the curvature radii trough a lens (for a “thin lens” w2=w1)
w0,1
w0,2
L1
L2
1. know/measure the incident beam (w0,1 or w1,r1) 2. derive r2 [ as ( 1/f - 1/r1 )-1 ] 3. use w2=w1 [ “thin lens" ] 4. derive w0,2 [ propagation of a Gaussian beam over L2] (knowing both r2 and w2, from 2. and 3.)
Before (“object") and after ("image") the lens we have w0 /r =const. and also w0 /L =const. and we see in the next side how …
analogous of 1/p+1/q=1/f for geometrical optics
w1 w2
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 7: Propagation through a lens
<number>/38
To “enlarge" w0,1 with respect to w0,2, one must work with r1>r2 and hence with the lens more distant from w0,1 (L1>L2) then the distance from w0,2 (or for L1<L2 one has w0,1< w0,2)
f
Transformation of the radii of curvature through a lens (for a thin lens w2=w1)
w0,1
w0,2
L1
L2
After propagating through a lens the beam undergoes a magnification m=w0,2 /w0,1=r2 /r1=L2 /L1
If z>zR (z>>zR)  r1,2L1,2 and hence 1r1w1=w22r2  r1/w0,1 r2 /w0,2 w0,1 /w0,2r1 /r2L1 /L2 and w0,1 /L1w0,2 /L2
being  =/w0
w1 w2
r1,2 are not easy to measure while measuring L1,2 is simple
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 8: Collimation over a range ±z* through a telescope
<number>/38
*
*
w(z*)
Varying w0 we search the minimum w(z*), at fixed z* distance from the beam waist... We differentiate the expression of the spot size w respect to w0, or y=[w]2 respect to W=[w0]2 :
condition for collimation over a range ±z*

the half-width of the collimation range is
with w(z* )1.4w0
k
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 9: Beam-sizing of the laser spot after a telescope
<number>/38
*
*
w0,f
w0,f /w0Lf /d and w0 /w0,f  Z /F  w0  (Z /F)  (f /d) w0L
Spot magnification: m=w0 /w0L=(Z/d)(1/M) with M = F / f = wF / wf telescope magnification
Typically one has f<<F, and it is relatively easy to “adjust" the dimension w0 (f ) and the distance Z by slightly moving the ocular (lens with focal length f )
( in fact, in terms of relative variations: w0/w0 = f/f )
wf
wF
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 10: Example of collimation for an He-Ne LASER beam used in alignment
<number>/38
DATA: He-Ne LASER with plano-concave cavity (L=20 cm, ROC=1 m). We want to cover z*=20 m with minimum spot dimensions: evaluate the magnification m of the laser spot and the one M of the telescope.
From we obtain w0L=282 m  0.3 mm
From =20 m we obtain w0=2 mm (diam. 2w0=4 mm)
Imagine we use a telescope with ocular distance d=10 cm and we want to work with Zz*=20 m.
From w0  (Z /F)  ( f /d) w0L we get m=w0/w0L= 7.1 = (Z/d)/M as magnification of the laser spot, whereas the magnification of the telescope is M = F/f = (Z/d)/m = (20/0.1)/7.1 = 28
At 20 m from w0, beam size is D  2  1.41w0  2.8  2 mm = 5.6 mm
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 11: Telescope for alignment and marine channel directions
<number>/38
Typically an alignment system uses an He-Ne (0.5-2 mW) laser and a 50-mm diameter telescope with magnification M=20-50. In practice the laser beam can remain collimated in a range from a few tens to a few hundreds of meters.
Using a telescope with D=100 mm and a 10 mW He-Ne laser, the beam can be seen at a few miles distance:
2/3T
1/3T
T
prism
Imax=P/Aeye< MPE
Plot 3 square waves with different d.c. val. at left, center, right
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 12: Alignment with the laser level
<number>/38
When we need to measure the height h or angle  over a working surface (construction area, pool, rice field, ...)
A laser level distributes, over an area of radius 20-50 m, a beam “horizontal fan", at constant height, by changing the rotation angle
Typical laser level instrumentation, tripod mounted
We need to “level" the laser beam: laser+telescope shine vertically (from bottom) to a 45° mirror, or to a pentaprism, reflecting light at 90° from incidence and hence in the horizontal direction
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 13: Horizontal leveling of the laser level
<number>/38
The verticality reference is the normal to the surface of a fluid (water) in the bowl Reflected beam at the air-water interface is recombined with the launched beam and perfect alignment is observed trough interference at the detector (screen or 4-quadrant photodetector). With 2 tilt prisms launch in X and Y directions can be regulated
just the pentaprism is rotating: transforming the beam from vertical into horizontal
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 14: Beam centering on a target and Position-Sensitive photoDetectors
<number>/38
For less stringent applications, like in constructions, it is sufficient an eye alignment (xy1 mm)
For more accurate measurements, we use a photodetector to allow electric signal proportional to the alignment error. A feedback system provides the alignment control by minimizing the error signal.
The position-sensitive photodetector can be a special “photodiode” (4-quadrant photodiode, PSD sensor or even a CCD) or a normal photodiode coupled to a spatial reticule/mask (rotating reticule) transmitting light as a function of the impinging beam position
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 15: 4-Quadrant photodiode (position sensor)
<number>/38
In the depletion region of the p-n junction, incident photons produce a current that can flow toward 4 distinct electrodes (one for each circular sector S1, S2, S3, S4)
The 4 photocurrents can be combined to obtain two signals proportional to X and Y coordinates of the beam with respect to the photodiode center: SX=(S2+S4)-(S1+S3) SY=(S1+S2)-(S3+S4)
rPD=0.2-2mm gap: 5-10m
We can also normalize signals to P0S0=(S1+S2+S3+S4)
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 16: Extraction of X and Y coordinates from 4-Quadrant photodetector
<number>/38
Dependence of the coordinate signal SX (SY) from the coordinate value X (Y) of the laser (or light) spot. For small spot (w0<<rPD) response is squared with a small dead-zone at X=0 (or Y=0). For larger spot the signal is “linearized” (in the central region)
OP-AMP circuit (transimpedance conversion of photocurrents and voltage sum/subtraction) to achieve the coordinate signals SX e SY
Sensor output strongly depends on size and shape of the incident spot
w/rPD
Spatial localization accuracy on the 4-Q depends on Pspot and w and spot shape, and gap and rPD: X,Y=10%-3%rPD
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 17: PSD photodiode (scheme and principle)
<number>/38
Position Sensitive Detector is a normal PIN photodiode with thin p and n regions lightly doped (to enhance the series resistance of p and n volumes at the border of the depletion region) Incident spot of (X,Y) coordinate produces a photocurrent flowing from electrodes Y (cathode) to electrodes X (anode)
The current, passing trough regions p and n of high resistivity is divided with the partitions rule between two resistors. The difference in the detected currents on the same electrode pairs (X or Y) gives the coordinate (X o Y)
'Si' for =400-1100 nm with L=0.5-5 mm
left right
the photodiode is reverse bias polarized
High linearity over the whole measurement range
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 18: PSD photodiode (electrical model)
<number>/38
Rl=x* Rr=(L-x)* Rl+Rr=L* * is the resistivity per unit length (in the slightly doped p region)
we have current partitioning toward the two anodes A1 , A2 such as Iph=Il+Ir
Il
Rr
Rl
ANODES
I ZONE
Iph
Ir
Rl Rr
Iph
x (L-x)
A1 A2
with voltage
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 19: PSD photodiode (working equations)
<number>/38
Similarly
From the OP-AMP circuit we obtain
The output becomes independent from photocurrent Iph (and P) dividing for the sum signal X/Y=R(Ix/y1+Ix/y2)=RIph  measurement independent from P and responsivity ( ρ )
Iph=ρP varying with P (and also with ρ!)
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 20: Transformation from angular into spatial (position) coordinate
<number>/38
When we need to measure the arrival direction (angle) of the optical beam, we use a collecting lens with focal distance f and we observe the displacement (position) off-axis of the laser spot in the lens focal plane:
Transformation law between angular and spatial coordinate is: r = ftan( )  f for  << 1

f
r
L
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 21: Angular position sensor with 4-Quadrant photodiode
<number>/38
If the sensor is placed in the focal plane of a lens, angular coordinate is transformed into a corresponding deflection coordinate : X = FX and Y = FY
A position sensitive detector (4-Q, PSD, reticule) other than indicator of X and Y coordinates can be used to detect angular (X and Y) coordinates of the arriving beam
Field Of View FOV = rPD / F
F
Notes: 07/29/26
<number>
Dopo una breve introduzione sull’argomento e sulle principali caratteristiche degli oscillatori laser,
vedremo più in dettaglio la struttura di una sorgente laser, i principi fisici che permettono l’azione laser, e i risonatori ottici.
A questo punto descriveremo in dettaglio alcune proprietà caratteristiche dei fasci laser.
Passeremo quindi alle misure della potenza ottica indicando metodi e strumenti adatti allo scopo.
Di seguito vedremo come si effettua la caratterizzazione del profilo spaziale e della divergenza di un fascio laser.
Infine illustreremo metodi e strumenti per la misura della lunghezza d’onda e dello spettro di emissione.
Così si concluderà la prima parte di questo intervento.

## Slide 22
<number>/38
Position Sensing with Reticules
Position sensing by a rotating reticule: light from a bright spot at the angle  is imaged by the objective lens on the focal plane, where it is chopped by the reticule placed in front of the photodetector. By comparing the phase-shift of the square waveform from the photodetector and of a reference, the angular position 0 of the source is determined. The amplitude of the signal, Vsignal , carries information on the polar coordinate , similar to that of the quadrant PD.
ρ
RPD
Transformation from angular into spatial coordinate (lens focal plane) and measurement of spatial coordinate (x,y) from polar coordinates (, =0)
Notes: 07/29/26
<number>
Sometimes, it may happen that we cannot use 4-quadrant or PSD PDs and merely have available a normal single-point detector. We can again realize a position-sensing, by placing the detector behind a rotating reticle. Reticles have been developed and used since the early times of thermal-infrared techniques, to track hot spots with single-point detector. In its simplest form, the reticle is a half-transparent and half-opaque disk, as illustrated in slide. When put into rotation, it actually works as a chopper of the radiation reaching the photodiode located in the focal plane.
Thus, if we have a single bright spot in the field of view, the photodiode current will be modulated into a square wave.The information about the angular coordinate 0 of the source is contained in the phase shift of the signal waveform respect to a reference square wave at 0=0.
It is easy to get this reference square wave, for example by a micro-switch or a LED-and-photodiode combination placed on the edge of the reticle, as shown in slide. The radial coordinate  can also be determined, by looking at the amplitude Vs of the square wave. With the same argument leading to the dependence plotted in Figure, we have the diagram of Vs versus reported at the bottom of Figure.
The plain black/white reticle works well with point-like sources, but is disturbed by the presence of extraneous extended sources in the field of view. Rejection to extended sources is improved by the rising sun reticle (next slide).

## Slide 23
<number>/38
Position Sensing with Reticules
The rising-sun (top) reticule provides a better suppression to extended sources of disturbance and digital counting of the angle .
The digital readout reticule (bottom) supplies both and  coordinates.
??? ???
fuori dal 50%, inizia alto T=1 e termina basso T=0
inizia a T=1 e termina a T=0
inizia a T=1 e termina a T=0
f  
T=1
T=0
5½ picchi (bianco con T=1) ??? 1.5 di troppo!!!
4½ picchi (bianco con T=1) ??? 2.5 di meno!!!
in realtà il diagramma temporale è quasi corretto ma il disegno è errato (ci vogliono tanti T=0 quanti T=1 per dare in media T=0.5)
qui ci manca una “fettina” bianca
Notes: 07/29/26
<number>
In this reticle, half circle has 50% transmission, and half has 0 or 100%-transmission sectors, averaging 50% on the entire reticle. As a result, a point source gives a response with large amplitude Vs, whereas details larger than the sector width have Vs≈0 and only add a continuous component to output.
The readout of the angle coordinate  can be made digital, by counting the periods elapsed between the signal down-going edge (electrical angle 0) and the reference down-going edge (electrical angle ) see the waveforms in slide. Another interesting reticle allowing an all-digital readout of coordinates is the digitizing –sector reticle . Here, the sectors are shaped according to a special radial profile. We choose the profile so that a point source at a radius  intersects a number of sectors proportional to 
Thus, by counting the number of periods contained in a complete 2-rotation of the reticle, we get the digits of the radial coordinate. The angular coordinate  is determined, as before, by the delay between the down-going edges of signal and reference, and is digitized when the delay is sorted out by period counting. As an example, in slide the signal for point 1 has 7 periods in a half turn while signal for point 2 has 4 because its radius is smaller. The angular coordinate 2>1 is seen to correspond to a different number of periods between  and . Using photolithographic techniques, we can easily attain a few-m detail on a few cm-side reticle, or a 10-3 to 10-4 relative resolution or potential number of sectors. This figure explains how a 10-bit resolution in the digital readout of ,coordinates is achieved with rotating reticles.

## Slide 24
<number>/38
angular distribution is I() = E02sinc2 /D first zeroes of sinc are at D=diff.=±D e Xzero=±FD
hence we can obtain D = FXzero
D
Measurements wires diameters from diffracted light analysis
electric field on the detector is the Fourier Transform of the aperture: FT of rectangle is sinc[ /(/D)]

D

For small wires (small D) we have Xzero large and vice versa (it is easier – higher sensitivity – to measure wires with small diameter)
=  /diff.
The distance between zeroes (or peaks) on the detector is proportional to 1/D
Notes: 07/29/26
<number>
In industrial applications and manufacturing, instruments for measuring dimension are common for testing and on-line control purposes. Diameter instruments are used mostly as the sensor of a process control in wire manufacturing. The wire may be a metal or a plastic wire extruded from a strainer or draw-plate, or an optical fiber as well. The on-line measurement allows a feedback action on process parameters, and the result is a better, tight control of tolerance of the fabricated wire.
The wire to be measured is passed in an aperture, where it is illuminated by the beam waist of an expanded laser beam. As usual, we use a He-Ne laser and a collimating telescope. The diffracted field is collected by a lens and its distribution is converted into an electrical signal by a PD placed in the focal plane of the lens. From this signal, the unknown diameter D is calculated. As well known from diffraction theory and recalled in App.A5, the distribution of diffraction from the wire is the Fourier transform of the wire aperture. Assuming a constant illuminating field E0, the field and the radiant power density diffracted at the angle are given by:
E() = E0 sinc D/andP() =E02sinc2 D/ Here, sinc  =(sin )/. The first zero of the sinc distribution is at =±1, corresponding to a diffraction angle zero =± DTo work out D, we use a lens (of focal F) to convert the angular distribution P() in a focal plane distribution P(X) to be scanned by the PD, with a scale factor is X=F.
To get D from the mesured P(X)= P0sinc2 XD/F we may look at different feature of the waveform P(X), e.g.: the main pulse width at half maximum, the secondary-maximum positions, the flex points, etc.

## Slide 25
<number>/38
Commercial instruments for wire diameter measurement, measurable diameters can range from 10 m (1% acc.) up to more than 2 mm (5% acc.)
aperture
telescope
He-Ne
lens and detector
Instrument for wire diameter measurement
The wire is passed trough an "U“ aperture: direct monitoring during production, with online correction during the spinning process
Notes: 07/29/26
<number>
But, taking into account non-idealities in the P(X) i.e.: (i) the finite size of the detector Wdet, (by which the P(X) distribution is averaged) and (ii), the strong peak coming from the non-diffracted beam and superposed to the useful signal near the origin X=0 (not shown in figure). IfDbeam is the beam diameter at the waist illuminating the wire, the non-diffracted peak has a width of the order of F/Dbeam, and an amplitude Dbeam2/D2 times higher than the wire diffraction amplitude.
Then, a good feature to look at in the P(X) distribution is the location of the first zeroes near the peak. These are positioned at =±D, or X=±FD. We may detect them e.g. with a linear-array CCD placed in the focal plane.
The CCD provides a signal i(t)= i0sinc2 vtD/Fwhere v is the scanning speed. By time differentiating the signal i(t), we get an i’(t) signal which passes through the zero level in correspondence to the minima of the sinc2 function. We can also get a digital processing of the measurement using a threshold discrimination of the i’(t) signal, to pick up the zeroes at time t=±F/vD, and gates to count clock transitions between start and stop triggers. If the clock frequency if fc, then the number of counted pulses is Ncount=2fcF/vD and we have a digital readout of the diameter D [however, we still require calculating a reciprocal].
In commercially available instruments, the allowed transversal movement of the wire is typically 2-5 mm with no degradation of other specifications.
A typical overall size of the diameter-sensing instrument is 50 by 20 by 10 cm.

## Slide 26
<number>/38
The diameter analyzer measures diffracted light from suspended particles within a fluid. At the cell exit a lens converts angular diffraction profile into a corresponding spatial profile in the focal plane ( R). A photodetector (scanned PD or CCD) measures I(R): the distribution of particle diameters, p(D), is calculated inverting
LAELS: Low-Angle ELastic Scattering electric field on the detector is the Fourier Transform of the aperture: FT of circle is somb[(R/F)/(/D)]
I(R) = I0 0-∞ somb2[(D/)(R/F)]p(D) dD with(R/F)=tan 
somb(x)=2[J1(x)]/x
Particle diameter measurement
PDF
[( /diff.)]
Notes: 07/29/26
<number>
Another instrument based on diffraction is the particle-size analyzer. With this instrument, we can measure the distribution of particle diameters in a fine-conglomerate mixture. Typical particle sizing range from manufacturing and industrial processes (ceramic, cement and alloys powders) to particulate monitoring in air and water, and to sorting of living material for medical and biological purposes. The measurement range usually extends from the sub-m particulate to relatively large particles, up to about 1 mm. The basic scheme of a particle-size analyzer is similar to the wire sensor, and with it we look at the small-angle diffraction or elastic scattering of light from the particles, so the scheme is classified as LAELS (low-angle elastic light scattering).
As a source, we use a low power (typ. 5mW) laser with a collimating telescope to project a nearly plane wavefront on the measurement cell. In the cell particles are kept in suspension by means of a mechanical stirrer or an ultrasonic shaker (PZT ceramic) toavoid flocculation. Each particle contributes to the far field distribution at  according to Fourier transform of aperture, giving A0 somb [(D/)sinin field and I0 somb2[(D/)sin]inpower density [ somb x= 2J1(x)/x]. The total power density is the integral of somb2 terms, weighted by p(D), the distribution of diameters:
I() = I0 0-∞ somb2[(D/)sin]p(D) dD.
Now, we wish to find the particle size distribution p(D), from the measured I(). The kernel of the Fredholm’s integral, somb2[(D/)sin],is a given term as we can compute it for any pair of  D. The problem is ill-conditioned, because p(D) is multiplied by the kernel and integrated, so that details in p(D) are smoothed out in the result I().

## Slide 27
<number>/38
Particle Size Measurement 2
Methods to solve for p(D) from measured data I()
- Analytical Inversion
p(D) = -[(4D)2/] =0-∞ K(Dsin/) d[3 I(Dsin/)] /I0
a theoretically nice result but impractical to be used.
- Least Square Method
Using a discrete approximation for p(D)=pk and I()=In and letting Snk= somb2[(Dk/)sinn]we get a set of equations:
In = k=1..K Snk pk (n=1..N)
N is the number of angular measurements performed on the intensity, K is the number of unknown diameters.We start with K<N and close the set adding N-K equations from the LSM condition, sought from:
2 = n=1..N [ In - k=1..K Snk pk]2 = min
Notes: 07/29/26
<number>
For example, very large particles affects only I() near ≈0, whereas very small ones give only a little increase of I() at large . Another source of error is the tacitly assumed constant scattering coefficient. This holds for large-particles, D>>, whereas for intermediate and small particles Qext varies appreciably (see App.A3). From these considerations, the measurement range best suited for the LAELS will normally go from a few m to perhaps several mm in diameter. The limit is Rayleigh approximation at small D, and the size of the PD at large D (with strong ≈0 signal).If we renounce to solve the equation exactly in all cases, we try to maximize the information content picked out from the experiment through the measurements of I(). To do so, we will repeat the measurement at as many angles as the outcomes I() are appreciably different. With a I() set, the kernel integral will limit resolution to a certain value, beyond which solution becomes affected by a large oscillating error. Then, we optimize the solution by increasing the number of D’s until the computed p(D) starts being affected by oscillation errors.
Let us now briefly discuss the mathematical approaches to solve the inversion problem given by integral equation.
Analytical Inversion. Difficult to use because requires integrating I(on from 0 to ∞ whereas Rayleigh regime are valid only for ≈0. In the range 10 to 50-m and with =0.633m, the method works nicely if measured data is very clean and accurate, that is affected by an error of 1% or less.
Least Square Method. Using a discrete approximation, we may write a set of linear equations and then apply the least-square method (LSM) to improve the stability of solution.

## Slide 28
<number>/38
Particle Size Measurement 3
Taking the derivative respect pk‘s and equating to zero gives:
(2)/pk = n=1..N 2[ In - k=1..K Snk pk](-Snk)
and rearranging we get
Jh = k=1..K Zhk pk (h=1..K)
where we have let Jh =n=1..N InSnh and Znk= n=1..N Snk2
Now, the number of equations is equal to the number of unknown and we can solve for pk with standard algebra.
Usually, the range of diameters of interest may be large (for example, two decades from 2 to 200m) but the number of affordable diameter is modest (e.g. K=6-9) at ±10% accuracy.
Notes: 07/29/26
<number>
To do so, we write the integral as a summation on the index k of diameter Dk, and repeat the equations for as many variables n of the angle n.
The matrix of known coefficients connecting n and Dk is the kernel Snk:
Snk= somb2[(Dk/)sinn]= 4J12[(Dk/)sinn][(Dk/)sinn2
The range of variables n and k is n=1..N and k=1..K, and the associated variables are In=I(n) and pk=p(Dk). With this, we get:
In = k=1..K Snk pk (n=1..N)
Here, the number of equations N may be different from the number of unknown K. Usually, N is the number of measurements, and may be usually 50-100 if we use an array o a CCD. The number K of unknown D’s is variable as we wish the largest number separate diameters p(D) that has no appreciable ringing (typ. K=6-20). To solve for the unknown pk, we bring the number of unknown to coincide with the number of equations, with the aid of the LSM. By the LSM, we require that the solution pk is such that the error 2, or mean square deviation of the computed values  Snk pk and measured ones In is a minimum: 2 = n=1..N [ In - k=1..K Snk pk]2 = min. We shall then set to zero the partial derivative of the error2, respect to each value pk of the unknown:
(2)/pk = n=1..N 2 [ In - k=1..K Snk pk] (-Snk). By rearranging we get:
Jh = k=1..K Zhk pk where we have let: Jh =n=1..N InSnh and Znk= n=1..N Snk2
Using the LSM, the accuracy of solution improves and the range of p(D) is larger, respect to the analytical inversion. However, if data are affected by errors or the number of diameters is excessive, then the error of the solution increases. Also, the error may be large if the waveform p(D) is bimodal or contains secondary peaks.

## Slide 29
<number>/38
Particle Size Measurement 4 *
-Iterative Methods. They are based on the following approach: if the set of diameter pk is correct, it should give the measured distribution In.calc= kCnk pk. If these values In.calc differ from experimental values Ik.meas, then we may expect to approach the solution if we multiply pk by Ik.meas/Ik.calc.
Using pk+1 = Ik.meas/Ik.calc pk and repeating an adequate number of times, pk should converge to the correct solution (there is no clear sign of convergence, however) A refinement of Chahine’s method consists in weighting the iteration by the normalized kernel, Snk/n=1..NSnk, using
pk+1 = (Snk/n=1..NSnk)(Ik.meas/Ik.calc) pk
In this way, spurious peaks found in Chahine’s method are suppressed, and resolution and dynamic range are improved
Notes: 07/29/26
<number>
Thus, one chooses a reasonable number of diameters to get the best result. A strategy is to increase the K of diameters and repeat the calculation until in the new result oscillations or wrong features start to show up. Usually, the range of diameter of interest may be large (typ, two decades from 2 to 200m) but the number of affordable diameter is modest (e.g. K=6). Of course, the cumu-lative distribution P(D) looks more regular than the density function p(D).
Other Linear Methods. The basic LSM we have outlined above is the starting point for several extensions. A straight example is weighting of terms contributing to the total error 2, adding in the equation a multiplying factor wn that is taken =1 where the measured In is clean (or, has a good S/N ratio), and <1 where In is noisy. Of course, the choice of the exact weight is somehow arbitrary, or left to our knowledge of the powder nature.
Iterative Methods. The prototype is Chahine’s method used to invert Fredholm’s equation in a variety of applications. We start letting K=N, that is, using a number of unknown variables pk equal to the number of measured intensities In (K=N is also provided by the application of the LSM, first). Now, if the set of diameter distribution pk is correct, it should give the measured distribution In.calc= kCnkpk. If the set of calculated values In.calc differs from the experimental values, then we may expect to approach the solution by multiplying pk by Ik.meas/Ik.calc, where Ik.meas are the measured values, or explicitly: pk+1 = Ik.meas/Ik.calc pk. By repeating the procedure, pk should converge to the correct solution. The trial values of pk may be either an estimated distribution or the result of a LSM calculation. Chahine’s method is definitely better than the normal LSM. Errors are reduced by a factor ≈3..5, and the range of D’s is increased. 

## Slide 30
<number>/38
Particle Size Measurement 5 *
Common errors in the PSM: finite size of detector, beam waist effects, lens vignetting, and undiffracted beam (=0), important for small (large D).
Better than a stop to block it out, we can use the filtering known as reverse Fourier-transform illumination, with a convergent beam to illuminate the cell. Diffracted rays (dotted lines) are focused on axis, and pass through the pinhole, whereas undiffracted rays arrive out-of-axis and are blocked.
Notes: 07/29/26
<number>
Several sources of error influence the results. The finite size of PD has been already considered. Another error comes from the undiffracted beam at =0, which requires a stop on the focal plane (omitted in figure to avoid confusion). Even using the stop, some light inevitably leaks aside on the detector, affecting the ≈0 measurements. To get rid of it, we can use the filtering arrangement known as reverse Fourier-transform illumination. Light projected by lens L1 is made to converge at a focal plane position. The contribution diffracted at the angle  reaches the focal plane of L1 at position x=F with rays parallel to the optical axis. Instead of reading the intensity in the focal plane, we place there a lens L2 and perform a Fourier transform of the incoming angular distribution. All the -diffracted rays arriving parallel to the optical axis are focussed on the axis of L2, whereas undiffracted light arriving at an angle reaches the focal plane out of the axis. With a pinhole at focal plane of L2, the diffracted contribution passes and the undiffracted is blocked out. Lens L3 re-transforms the filtered distribution to one with collimated rays.
Because of the scattering suppression, the arrangement of slide is better of a stop in the focal plane, and we can measure down to small angle (typ. <0.1mrad). Accordingly, the range of large diameters that can be reconstructed is expanded up to several hundreds m or even up to the mm.

## Slide 31
<number>/38
Particle Size Measurement 6
A modern, general purpose particle-size analyzer based on diffraction performs diameter measurements from 1 to 2500 m [by CILAS, France]
Notes: 07/29/26
<number>
About the source, we need one with a high radiance and a wide spectral emission, because the minimum detectable signal depends on radiance, and the minimum measurable size depends on the shortest wavelength available. To cover the visible and UV range, a cheap choice is a halogen lamp with 3000-3300-K color temperature. The lamp output is collimated by a lens and filtered by a monochromator. The output beam can be either combined with the laser beam of the LAELS by means of a wavelength-selective beamsplitter, or used as stand-alone source. The detector to be used is usually a photomultiplier, well suited for the spectral range UV-visible, and providing the best sensitivity even in the case of small particulate concentration.
An example of a modern particle-sizing instrument is shown in this slide. This instrument is the technical evolution of a first product released in 1971.

## Slide 32
<number>/38
Particle Size Measurement 7
An example of an-easy-to-get particle size pdf p(D) and cdf P(D) distribution measured by a commercial instrument (courtesy of CILAS)
Notes: 07/29/26
<number>
Thus, one chooses a reasonable number of diameters to get the best result. A strategy is to increase the K of diameters and repeat the calculation until in the new result oscillations or wrong features start to show up. Usually, the range of diameter of interest may be large (typ, two decades from 2 to 200m) but the number of affordable diameter is modest (e.g. K=6). Of course, the cumu-lative distribution P(D) looks more regular than the density function p(D).
Other Linear Methods. The basic LSM we have outlined above is the starting point for several extensions. A straight example is weighting of terms contributing to the total error 2, adding in the equation a multiplying factor wn that is taken =1 where the measured In is clean (or, has a good S/N ratio), and <1 where In is noisy. Of course, the choice of the exact weight is somehow arbitrary, or left to our knowledge of the powder nature.
Iterative Methods. The prototype is Chahine’s method used to invert Fredholm’s equation in a variety of applications. We start letting K=N, that is, using a number of unknown variables pk equal to the number of measured intensities In (K=N is also provided by the application of the LSM, first). Now, if the set of diameter distribution pk is correct, it should give the measured distribution In.calc= kCnkpk. If the set of calculated values In.calc differs from the experimental values, then we may expect to approach the solution by multiplying pk by Ik.meas/Ik.calc, where Ik.meas are the measured values, or explicitly: pk+1 = Ik.meas/Ik.calc pk. By repeating the procedure, pk should converge to the correct solution. The trial values of pk may be either an estimated distribution or the result of a LSM calculation. Chahine’s method is definitely better than the normal LSM. Errors are reduced by a factor ≈3..5, and the range of D’s is increased. 

## Slide 33
<number>/38
Particle Size Measurement 8 *
In the Rayleigh regime r<<, the scattering is nearly isotropic in angle and the extinction factor Qext varies as (r/)4.
When r increases up to about r ≈(intermediate regime)the scattering function f() is mainly forward and the extinction factor increases up to Qext≈2-4.
For r >>we enter in the Mie regime, extinction Qext is nearly constant (in ) at ≈2 and f() is strongly peaked forward
Qext tells how much the light extinction cross section (due to scattering) is larger than the physical area (r2) of the diffusing particle
Notes: 07/29/26
<number>
At the other end of the measurement range (large  or small D), errors are also due to the Fraunhofer approximation D>>. Errors start becoming significant at, say, D≈2-5, and thus the practical range of measurement for particle sizing based only on the low-angle light scattering (LAELS) is typically 2…500m.
The range on small particles is extended by taking advantage of the Mie (D≈) and Rayleigh (D<<) scattering regimes.
These are described by the appropriate scattering function f() and extinction factor Qext (App.A3). In the Rayleigh regime, the scattering is nearly isotropic in angle and the extinction factor Qext varies as (D/)4. When D increases up to about D≈the scattering function peaks forward and the extinction factor peaks up to ≈2-4.
Now, we can supplement the LAELS measurement with a measurement of light scattered from the cell at a fixed angle, large enough to be out of the range of LAELS data, e.g., looking at the cell from ≈45°, so that the detector is safely away the undiffracted. To collect information on the p(D), we now scan  instead of the diffraction angle. By varying the ratio D/, the extinction factor Qext(D,,n) varies and the scattered power too.

## Slide 34
<number>/38
Particle Size Measurement 9 *
Another method is SEAS (Spectral Extinction Aerosol Sizing). It is based on measuring light scattered from the cell at a fixed angle, while scanning  instead of . By varying the ratio D/, the extinction factor Qext(D,,n) varies and the scattered power too, according to:
I(,45°) = f(45°) (/4) I0 0-∞ Qext(D,,n) p(D) dD
where f()=scattering function, Qext=extinction factor. The equation is the counterpart of that for extinction-related measurement, and all the methods of inversion of the Fredholm’s integral can now be applied on Dk and n. With SEAS we may to go down to 0.02–0.1m as the minimum measurable size, overlapping with the LAELS low-range (≈ 2-5m).
A last method is the Dynamical Scattering Size Analyzer (DSSA), useful for very small (1..100-nm) particles. Based on the frequency shift due to Doppler effect (ko-ki)v, it is measured by the time-domain autocorrelation function C()=(1/T)0-Ti(t)i(t+)dt which depends from the diffusion constant  of particles according to: C()=C0 exp – (ko-ki)2
Notes: 07/29/26
<number>
For a density distribution p(D) of diameter, and given an extinction factor Qext(D,,n) at the measurement wavelength , the power density collected in a solid angle  around =45° is:
I(,45°) = f(45°) (/4) I0 0-∞ Qext(D,,n) p(D) dD
where f() = scattering function and Qext = extinction factor (App. A3). This method of particle sizing is called SEAS -Spectral Extinction Arosol Sizing). With the computation of the distribution p(D) from this equation, we now go down to 0.02–0.1m as the minimum measurable size, and are able overlapping the minimum of LAELS (≈ 2-5m).
A last method worth to be mentioned is the dynamical scattering size analyzer (DSSA), useful for measurements of very small (1..100-nm) particles. Different from all previous techniques when particle is very small, we use now that the scattered light is frequency shifted. The shift is due to the Doppler effect (ko-ki)v, or equivalently by the interferometric phase (ko-ki)s, of the particle displacement s observed from the direction ko and illuminated from kI
The shift is measured by a frequency-spectrum analysis, or better, by a time-domain autocorrelation measurement, of the detected signal. For example, the autocorrelation function C()=(1/T)0-Ti(t)i(t+)dt is found to depend from the diffusion constant  of the particles, as C()=C0 exp – (ko-ki)2
From the measurement of the exponential decay of C(), the constant  is determined. Then, we use the relation  =kT/2D and determine the diameter D, once the viscosity of the particle in the surrounding medium is known.

## Slide 35
<number>/38
Particle Size Measurement 10
A SEAS particle size analyzer uses scattering data at 135° to sort submicronic particulate (typ. of metropolitan area pollutants) from 0.02 to 0.1 m [by CILAS, France]
Notes: 07/29/26
<number>
About the source, we need one with a high radiance and a wide spectral emission, because the minimum detectable signal depends on radiance, and the minimum measurable size depends on the shortest wavelength available. To cover the visible and UV range, a cheap choice is a halogen lamp with 3000-3300-K color temperature. The lamp output is collimated by a lens and filtered by a monochromator. The output beam can be either combined with the laser beam of the LAELS by means of a wavelength-selective beamsplitter, or used as stand-alone source. The detector to be used is usually a photomultiplier, well suited for the spectral range UV-visible, and providing the best sensitivity even in the case of small particulate concentration.
An example of a modern particle-sizing instrument is shown in this slide. This instrument is the technical evolution of a first product released in 1971.

## Slide 36
<number>/38
Particle Size Measurement 11
A modern particle-size analyzer based on diffraction and extinction (LAELS + SEAS), performs diameter measurements
from 0.05 to 2500 m [by CILAS, France]
Notes: 07/29/26
<number>
About the source, we need one with a high radiance and a wide spectral emission, because the minimum detectable signal depends on radiance, and the minimum measurable size depends on the shortest wavelength available. To cover the visible and UV range, a cheap choice is a halogen lamp with 3000-3300-K color temperature. The lamp output is collimated by a lens and filtered by a monochromator. The output beam can be either combined with the laser beam of the LAELS by means of a wavelength-selective beamsplitter, or used as stand-alone source. The detector to be used is usually a photomultiplier, well suited for the spectral range UV-visible, and providing the best sensitivity even in the case of small particulate concentration.
An example of a modern particle-sizing instrument is shown in this slide. This instrument is the technical evolution of a first product released in 1971.

## Slide 37
<number>/38
Particle Size Measurement 12
A second example of particle size pdf p(D) and cumulative P(D) of a bi-modal distribution, more difficult because with both small and large particles, as measured by a commercial instrument (courtesy of CILAS)
Notes: 07/29/26
<number>
Thus, one chooses a reasonable number of diameters to get the best result. A strategy is to increase the K of diameters and repeat the calculation until in the new result oscillations or wrong features start to show up. Usually, the range of diameter of interest may be large (typ, two decades from 2 to 200m) but the number of affordable diameter is modest (e.g. K=6). Of course, the cumu-lative distribution P(D) looks more regular than the density function p(D).
Other Linear Methods. The basic LSM we have outlined above is the starting point for several extensions. A straight example is weighting of terms contributing to the total error 2, adding in the equation a multiplying factor wn that is taken =1 where the measured In is clean (or, has a good S/N ratio), and <1 where In is noisy. Of course, the choice of the exact weight is somehow arbitrary, or left to our knowledge of the powder nature.
Iterative Methods. The prototype is Chahine’s method used to invert Fredholm’s equation in a variety of applications. We start letting K=N, that is, using a number of unknown variables pk equal to the number of measured intensities In (K=N is also provided by the application of the LSM, first). Now, if the set of diameter distribution pk is correct, it should give the measured distribution In.calc= kCnkpk. If the set of calculated values In.calc differs from the experimental values, then we may expect to approach the solution by multiplying pk by Ik.meas/Ik.calc, where Ik.meas are the measured values, or explicitly: pk+1 = Ik.meas/Ik.calc pk. By repeating the procedure, pk should converge to the correct solution. The trial values of pk may be either an estimated distribution or the result of a LSM calculation. Chahine’s method is definitely better than the normal LSM. Errors are reduced by a factor ≈3..5, and the range of D’s is increased. 

## Slide 38
<number>/38
Particle Size Measurement 13
A third example of particle size pdf p(D) and cumulative P(D) of a distribution with two populations of very large particles (powders) as measured by a commercial granulometer (courtesy of CILAS)
Notes: 07/29/26
<number>
Thus, one chooses a reasonable number of diameters to get the best result. A strategy is to increase the K of diameters and repeat the calculation until in the new result oscillations or wrong features start to show up. Usually, the range of diameter of interest may be large (typ, two decades from 2 to 200m) but the number of affordable diameter is modest (e.g. K=6). Of course, the cumu-lative distribution P(D) looks more regular than the density function p(D).
Other Linear Methods. The basic LSM we have outlined above is the starting point for several extensions. A straight example is weighting of terms contributing to the total error 2, adding in the equation a multiplying factor wn that is taken =1 where the measured In is clean (or, has a good S/N ratio), and <1 where In is noisy. Of course, the choice of the exact weight is somehow arbitrary, or left to our knowledge of the powder nature.
Iterative Methods. The prototype is Chahine’s method used to invert Fredholm’s equation in a variety of applications. We start letting K=N, that is, using a number of unknown variables pk equal to the number of measured intensities In (K=N is also provided by the application of the LSM, first). Now, if the set of diameter distribution pk is correct, it should give the measured distribution In.calc= kCnkpk. If the set of calculated values In.calc differs from the experimental values, then we may expect to approach the solution by multiplying pk by Ik.meas/Ik.calc, where Ik.meas are the measured values, or explicitly: pk+1 = Ik.meas/Ik.calc pk. By repeating the procedure, pk should converge to the correct solution. The trial values of pk may be either an estimated distribution or the result of a LSM calculation. Chahine’s method is definitely better than the normal LSM. Errors are reduced by a factor ≈3..5, and the range of D’s is increased. 