## Slide 1: “Optical Measurements” Master Degree in Engineering Automation-, Electronics-, Physics-, Telecommunication- Engineering
Optical Telemeters Prof. Cesare Svelto Politecnico di Milano
Some pictures are taken from the Book “Electro-Optical Instrumentation: Sensing and Measuring with Lasers” by Prof. Silvano Donati

## Slide 2: Summary
Measurement principles and applications
Triangulation - passive - active
LIDAR (LIght Detection And Ranging)
Time Of Flight (TOF) - pulsed - Continuous Wave (CW) [with sine modulation] - power budget of a laser telemeter and system equations - timing and optimal filtering, noise and accuracy, ambiguity - optics (launch/receiving), instrumental development

## Slide 3: Measurement principles in Telemetry (1/2)
tele-metry = distance-measurement (or also measurement at distance) we measure the distance L between the instrument and a remote target ( range-finding and range-finder )
1) by triangulation (trigonometric method)
the target is "triangulated" from two points apart D on the same baseline (see measurement of the distance of the stars); measuring the angle between the two lines of sight one gets the distance as LD/ (L=D/tg)
2) by Time Of Flight (measurement by counting a time interval)
pulsed laser or CW sine modulated ( fm) laser
T = 2L/c  L = c/2  T  T ( "2L" for a round-trip path)  = 2fm  T  /2=fm/(c/2L)  L = c/2   / 2fm = m/2   / 2   “ counting in terms of m /2 ”
( measurement depends on res./acc. on T and  , for CW also on fm e m )

## Slide 4: Measuement principles in Telemetry (2/2)
3) by interferometry (by means of counting optical wavelengths)
a laser beam (monochromatic) is sent to the target and the returning light is coherently detected, by beat note analysis on a photodetector; the detected signal goes as cos(2kL), with k=2/, and from the phase of the cosine function we can "count" the distance increment in terms of /2 and its fractions, from 0 to L or for small variations L starting from a fixed L*
 = 2kL   =2(2/L  L =/2 / 2  
“ counting L in terms of /2 ”
cos [ 2· L / (/2) ] ( resolution depends on laser’s  )
with  typically 0.5 m (VIS) we count L in terms of L=/2=250 nm (resolving “just”  =2) but with  = o /2 we obtain L=125 nm or 60 nm and less…
tele-metry = distance-measurement (or also measurement at distance) we measure the distance L between the instrument and a remote target

## Slide 5: Measurement fields for Optical Telemeters
T E L E M E T E R S
Distance and displacement measurements
WITH SINE MODULATION
(electrical phase shift meas. on mod. light)
topography, medium range
PULSED
(meas. time of flight)
geodesy, radar, long-range
INTERFEROMETRY
(meas. optical 
coherent detection)
very high-resolution
BY INTENSITY MODULATION
(optical mod. incoherent meas.)
BY TRIANGULATION
(meas. optical P and beam position)
short-range
[0.1-10 m]
[L=100-10 nm]
[0.1-10 km]
[1-1000 m]

## Slide 6: Measurement method by triangulation
Measurement becomes less accurate over long distance (in practice for L>>D). In fact, if the detection angle gets small (<10 mrad  0.5°) rel. uncertainty / increases

TELEMETER TARGET

## Slide 7: Passive optical triangulator
sensitivity of L with 
error or unc. or res. (absolute)
error or unc. or res. (relative)
D/L=tan
from angular meas. we get the distance L
note that L increases as L2 res. gets worse with increasing distance
EYE
UNCertainty
quantized meas. (limited res.)
/2
L non-linearly depending on viewing angle 
L2 or 1/
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 8: “Optical lever” on the mirror
/2






/2
+ = 90°
+ 2= 90°
- = 45°
from  we get +  = 45°
from  we get + = 45°
subtracting the two members, do obtain = 
45°
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 9: Resolution and accuracy in a passive optical triangulator (examples)
Accuracy/resolution of distance measurement (L) depend on accuracy/resolution of the angle measurement (
For example, with a micrometrical-screw goniometer we can resolve  1.5 mrad (0.08 °) while with an angular encoder we can achieve  0.05 mrad (0.0029 °) and  = 2
Ex.: for L=1 m we choose D=10 cm  D/L=0.1 rad
Performance is good until D/L   is not too small and hence for short ranges (L=0.1-10 m)
if for L=100 m we choose D=1 m  =D/L=0.01 rad
it would be insane to keep D=10 cm because it would be =1 mrad
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 10: “Active” (laser) optical triangulator
We can remove moving parts (no goniom. with respect to passive triangulator) and we achieve a very quick and accurate response, very repeatable
We use visible  for simplicity of “target viewing” (He-Ne at 633 nm or LD-VIS or Nd:YAG 2)
The laser beam undergoes a round trip path from telemeter to target. 1D measurement with optical position sensor (2Q/PSD/CCD) of the angle  between going and returning beam. Receiving optics is off-axis at a distance D from launching optics (so angle  is converted into displacement x): we then retrieve L=D/tan
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 11: Laser triangulator or active triangulator

Interference filter removes ambient light disturbance
fill L
frec
 is measured as displacement in the "rec“ lens focal plane
x
 = atan(D/L)=atan(x/frec) L = (D/x)frec 1/x “non-lin”
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 12: Image from a thin lens under “geometrical optics" [basics]
q
p
For an object at distance p=f (focal length) from the lens, image is formed to the “infinity" i.e. at a distance q=
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 13: Dimensioning of the laser spot size in the active triangulator [calculus steps]
optical axis


L1
L2
h1
h2
wrec= (frec /fill)wL
h1=wL and L1=fill h2=wT and L2=L
toward target
h1=wT L1=L h2=wrec L2=frec
toward receiver
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 14: Measurement equations for the active optical triangulator (1/2)
Let x be the distance of the received spot on the CCD from the receiving lens optical axis (which is off-set at a fixed distance, D, from the launching optical axis)
For a variation LL we get a corresponding var.   and x x (the lens converts  into x and  into x)

conversion from angle to displacement

distance measured as an agle
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 15: Measurement equations for the active optical triangulator (2/2)
L measured from the position x on the CCD is
and finally
once again as for the passive optical triangulator
hence, by differentiating in L and in x, we get
Same formula as for passive triangulator but with x and x instead of  and 
x is now electronically measured by a CCD and we don’t use a goniometer to measure 
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 16: Exercise on the laser triangulator (“known“ formulas: only calculations)
DATA: as in the case of passive optical triangulator, we work with D=10 cm (and frec=25 cm) for L=1 m and we now consider wL=5 m and wCCD=10 m:
If we resolve x =10 m ( wCCD) on the photodetector,
( L=400 m )
( for L = 1 m )
Remember how for the passive triangulator it was  3 mrad (micro-screw goniom.) and  0.1 mrad (angular encoder)
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 17: Exercise on the active triangulator (with data, calculations and steps to get wrec)
DATA: L=1 m wL=5 m fill=125 mm frec=250 mm
optical axis


L1
L2
h1
h2
wrec= ( frec /fill)wL=10 m  wCCD
h1=wL e L1=fill h2=wT e L2=L
h1=wT L1=L h2=wrec L2=frec
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 18: Interpolation in the laser triangulator
Exploiting the spatial extension of the laser spot on the CCD, we can interpolate over more bright pixels and even resolve a sub-pixel laser spot position (e.g. x=0.2wCCD or even less) with a resulting improvement in angular and distance resolution
EXERCISE (for home…):
Using a laser triangulator with Gaussian laser spot large wrec=50 m on a 1024 pixel CCD (with 12 bit amplitude resolution and wCCD=10 m), we want to retrieve the position of the “spot center" obtained by interpolating over bright pixels
Spatial resolution x of the CCD limits angular resolution  and hence resolution L in the measurement of distance L
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 19: Exercise on the laser triangulator
QUESTIONS:
- if the telemeter laser is an He-Ne laser at 633 nm, what kind of CCD should we use? why?
- how many and which pixels on the CCD are “well lit" when the “background light" covers 1/100 (in amplitude) of the measurement dynamic range?
- how shall me measure the position of the spot center on the CCD? How much wide is the “visible” spot?
- which are the practical limits to the accuracy?
- imagine we can achieve a resolution of 0.1 pixel and calculate the absolute resolution of the telemeter at the minimum measurable distance Lmin=10 m
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 20: Exercise on the laser triangulator
[in general one pixel is lit if its signal level brings its output voltage to a greater than zero (just quantization limit) or here the pixel is well lit when its "signal" level is > 1/100 of the peak/dynamic-range of the whole optical signal (limits due to “noise" and background light)]
ANSWERS:
- for a red He-Ne laser we can conveniently use a Si CCD, sensible in the visible range and inexpensive
- To calculate how many and which pixels on the CCD are “well lit", we must before define what we mean for “well lit": since the single pixel can resolve N=2n=212=4096 levels of photocurrent and hence incident optical power, we can say that a pixel is well lit (SNR=1) if the current signal is equal to the minimum detectable current (due to quantization or electronic noise of the receiver + “background light")
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 21: Exercise on the laser triangulator
We hence can calculate
r kwrec with k =[0.52.3log10M]0.5
clearly r and wrec correspond to a certain number of pixels
The optical power on the single pixel is the optical intensity times the pixel area (precisely one should integrate the intensity over the pixel surface)
Optical intensity is decreasing as exp(-2r2/w2rec) getting farer from the peak (in r =0). So we obtain an 1/M part of the peak value when 2r2=w2recln(M) or equivalently r/wrec=(0.5lnM)0.5=[0.52.3log10M]0.5
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 22: Exercise on the laser triangulator
we hence obtain r2wrec=250m100m corresponding to 10 pixels each of size 10 m (starting from the Gaussan center). The total number of well-lit pixels is finally 20 pixel (10), for a "visible" spot size (diameter) of approximately 200 m
just quantization: we get 1/4096  1/4000 of the peak value for 2r2=w2recln(4000) ( 4000 amplitude levels for n=12 bit) r/wrec=(0.5ln4000)0.5=[1.15log104000]0.5=[1.153.6]0.52
with noise and background (at 1/M=1/100 from peak): we get 1/100 of the peak value for 2r2=w2recln(100) r/wrec=(0.5ln100)0.5=[1.15log10100]0.5=[2.3]0.51.5 and r 75m with a well-lit spot of about 150 m diameter or 15 pixel
for 1/M=1/10 of peak, r  1.1wrec [as we know exp(-2)=13 %1/10]
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 23: Exercise on the laser triangulator
- The CCD is wide xmax=102410m1cm and, considering that x/xmax=/max=-L/Lmin, the resolution of the measure is L=Lmin(x/xmax)= =10m(1m/1cm)=1mm [at 10 m distance it is 10-4]
- The spot position on the CCD can be obtained by a weighted average of the Gaussian profile “points”, maybe after subtracting background level, and preferably by the average of only well-lit points; or by least squares fitting with function (Gaussian + offset): we can imagine achieving x=0.1pixel=1m
- Limits to the accuracy are set by noise at the photodetector (ext. light, shot noise, CCD dark current, additional noise: quantization/electronic) leading to a wrong estimate of the center position of ideal Gaussian
using the photovoltage as pixel weight
Notes: Possiamo cominciare definendo i diversi intervalli di frequenza/lunghezza-d’onda che rappresentano la regione spettrale delle “frequenze ottiche”.
Ricordiamo la relazione fondamentale, ( lambda = ci su ni ), che lega lunghezza d’onda e frequenza di una radiazione elettromagnetica, dove “c” è la velocità di propagazione della luce nel mezzo considerato.
Partendo dalle frequenze più basse, e dunque dalle onde “più lunghe”, possiamo individuare la regione delle onde millimetriche, con lunghezza d’onda tra i 10mm e 1mm; salendo in frequenza, entriamo nel campo dell’infrarosso, lontano e medio, che si estende dai 100 ai 2.5um, ETC. .

## Slide 24: Time Of Flight (“TOF”) telemeters (principles and working equations)
Laser radiation, by means of optical pulses, undergoes a round-trip path 2L (forth and back) in a time T (TOF or Time Of Flight), traveling at light speed c  3 108 m/s

## Slide 25: Time Of Flight (“TOF”) telemeters (principles and working equations)
Example: to get L =1 m we need T=21m/3108 m/s 7 ns limit for a Q-switched laser; for shorter  values we need a mode-locked laser; power...)
for L =1 mm  T7 ps… difficult to resolve sub-mm with conventional TOF
L is constant depending only on the time resolution T
L / L  1 / L improves as
L inreases

## Slide 26: Time Of Flight telemeters (length and time resolution)
Length resolution L in the measurement depends on the time resolution T and so also on pulse duration 
To resolve a time distance or interval T we must work with pulse duration<T and hence with “fast” photodetector electronics, having bandwidth B(1/)

## Slide 27: Time Of Flight telemeters (time interval measurement)
The measurement of a time interval T is achieved with an electronic counter, "counting" the distance between tstart (transmitted pulse) and tstop (pulse received), on the corresponding photodetected electronic signals. Position of pulses on the time axis is determined by a threshold discriminator (trigger) on the voltage waveform/pulses
Not always an analogue t falls exactly on a clock transition. So the measurement of t has the discrete resolution Tc of the electronic counter, with uncertainty uq(t)=(t)=Tc /
tstart
tstop
t
T
Tc
T = tstop – tstart  N TC
Tc

## Slide 28: Time Of Flight telemeters (measurement uncertainty of T=tstop-tstart)
Having uncertainty u(t)=uq(t) both on tstart and tstop then the combined accuracy on the measured time of fligh T is u(T) = [u2(tstop)+u2(tstart)]1/2 = uq(t) = TC/
In general, by choosing the clock period Tc short enough, the measurement uncertainty will depend on other factors (much more significant than the “small quantization”): in particular on the amplitude noise at the trigger input.
This noise depends on the circuit electronic noise and on the amplitude noise of the detected signal
If we start the clock, with period TC, exactly at tstart we then have u(tstart)=0 [ clock pulses starting with t=tstart ] and for the whole TOF we obtain u(T) = u(tstop) = TC/

## Slide 29: Time Of Flight telemeters (threshold discrimination and noise: 2)
The time of flight is measured as T = tstop - tstart and its variance is 2(T)=2(tstart)+2(tstop)2(tstop)
The location of pulses on time axis is obtained by a threshold discriminator (trigger) acting on the voltage signal S(t) at the photodetector output
Amplitude noise S becomes time noise t through the slope in the trigger point
tstop is more noisy
thres.
S
t
S
Detection of the light pulse providing tstop is “more noisy" (with lower SNR) since the light signal returning from the target is much weaker than the transmitted signal 2(tstop)>>2(tstart)

## Slide 30: CW telemeters (principle)
Optical power sine modulated at frequency fmod
We detect the phase delay  between detected signal (Pr) and transmitted signal (Pt)
P(t) = P0 [1+m sin( 2fmodt )]
T
Tmod=1/fmod
L = c/2  T = c/2  Tmod   / 2 = c/2   / 2fmod
P0 is the average power

## Slide 31: CW telemeters (working equations)
Measurement sensitivity (of the phase  on the distance L) gets higher for higher modulation frequency, BUT “if fmod is too high” we can run into measurement ambiguity
sensitivity tells how (direct measure) varies with a variation of the distance L
with fmod=10 MHz
and ()=2 mrad (1.2°)
we get (L)5 mm
Increasing fmod we can
measure smaller L

## Slide 32: Power budget in optical telemeters
Ps
Pr
Dcc
full divergence angle
In practical applications L >> fs, fr, Ds, Dr

## Slide 33: Cooperative target (reflecting) (1/2)
When the target is cooperative, e.g. corner cube reflector, it behaves like a mirror and hence the receiver sees the target at a distance 2L
The beam spot size (diameter) at distance 2L is s2L and hence the fractional received power (respect to transmitted power from the source), on a circular area with diameter Dr (receiving lens) set at distance 2L, is equal to:
ratio of the receiver area to received beam spot size (area)
Dr
D=s2L
L
D'=sL
infinite plane reflecting surface
if all the receiver is lit (D>Dr)
“areas ratio at the receiver”

## Slide 34: Cooperative target (reflecting) (2/2)
If the corner cube has a diameter smaller then the laser spot size on it (Dcc<sL) and the receiver collects all the reflected beam (i.e. “only corner cube cutting the beam") , we have:
Dr
Dcc
If in addition to the corner cube also the receiver is cutting the beam, we have again (like for the infinite plane reflector):
Dr
Dcc
The condition of “cutting receiver” is valid when Dr < 2Dccand hence ONLY when Dcc< Dr /2 the corner cube is effectively cutting the beam
Dr > Dcc+sL > Dcc+ Dcc = 2Dcc  Dcc < Dr/2
Dr
Dcc
Dr
2Dcc
areas ratio at the CC
it is like receiver
Dr=2Dcc
areas ratio at the receiver

## Slide 35: Solid angle
Def. # Radian  is the plane angle subtended by a circular arc, as the length of the arc (r) divided by the radius of the arc (R):  =r/R (1 rad is the plane angle where the arc is equal to the radius).
Def. # Steradian  is the solid angle subtended at the center of a sphere, as the area (S) of the cap divided by the squared radius of the sphere (R2):  =S/R2
S
R2
( r << R )

## Slide 36: Radiance of a Lambert diffusing surface
P
P
Radiant Intensity
radiance or brightness

## Slide 37: Non-cooperative target (diffusing)
When the target is non-cooperative, its illuminated surface, with area AT, is diffusing light with a diffusing coefficient  < 1
B is the target brightness (or radiance)
AT
 Ps


## Slide 38: Non-cooperative target (diffusing)
Naming r the solid angle (r the plane angle) by which the light diffused from the target is seen by the receiver, we have
being r = (Dr/2)/L
with a fractional received power
like for cooperative target
but with  instead of 1/s2
and obviously   1<<1/s2
angle of sight of the receiver (from the target)
and hence the power collected at the receiver is
independent from the lit area (spot size) on the target

## Slide 39: Power budget with diffraction and additional losses (optics and atmosphere)
Considering power losses due to Tx and Rx optics (Topt  1) and round-trip (2L) propagation in the atmosphere (Tatm 1)
In the end we can write a general expression
cooperative
non-cooperative
equivalent length
equivalent GAIN

## Slide 40: Gain of the optical telemeter
The optical telemeter gain can be G>>1 in the case of cooperative target (since s<<1)
if s=1 mrad and Topt1
in this case the expression is analogous to the “gain of the antenna" in a radio transmission ( where it is extremely important to have low divergence )
Instead, the optical telemeter gain is always G<1 in the case of non-cooperative target (typ.=0.5-0.1)
Good optics (antireflection coated at  laser) allow reflection losses <1%, at each air-glass interface, and absorption+scattering losses in the material (glass or quartz) <10-3  whole transmission Topt>0.98-0.91

## Slide 41: Attenuation coefficient
During its propagation (in the air), the laser beam undergoes absorption and scattering losses due to molecules or particulate always present in the atmosphere
Carefully avoiding molecular absorption peaks, we can approximately adopt =0.1km-1 for a very clear atmosphere, =0.3km-1 for clear atmosphere, =0.5km-1 for little haze, and >>0.5km-1 if foggy.
Tatm = exp ( - 2L ) =P(z=2L)/P(z=0)
from the law of
Lambert-Beer
=a()+s()=() attenuation coefficient
absorption
scattering (“diffused” light by molecules)
[ in the case of no absorption ()s() ]

## Slide 42: Atmospheric attenuation
Clearly, at any fixed , atmospheric transmission is exponentially decreasing with L (reducing received power Pr)
1 %
1 ‰

## Slide 43: Atmospheric attenuation (examples)
With very clear atmosphere, we can reach up to 20 km (and come back!) with an optical transmission 10%
With some haze, at a 10 km distance, transmission is 1%
With fog, just at 1 km distance, transmission is below 1‰
In order to have the highest Tatm, we must avoid some peaks of atmospheric absorption (with () highest and Tatm lowest): e.g. 0.70, 076, 0.80, 0.855, 0.93, 1.13 m:  used lasers are He-Ne (0.633 m) or Nd:YAG (1.064 m) or (532 nm) LD-GaAlAs (0.82-0.88 m)
(with =3.5 km-1 we get Tatm=exp(-7)10-3 at 1 km)
1
3.5

## Slide 44: Atmospheric attenuation (calculations)

## Slide 45: Atmospheric attenuation (examples)

Solar light spectrum reaching the Earth surface shows transparency windows and absorption peaks of the atmosphere
AM=(sin )-1 "Air Mass" where  is the arrival angle respect to the Earth surface (“to the horizon")  = Sun elevation
( A / W )
Note how for small elevation angles the solar light e.m. spectrum depletes of blu light (scattering -4) and enriches, relatively, of red light (less scatter)
VIS
sun at noon
sunrise or sunset
(sin )-1 BP/AP
just out of atmosphere

## Slide 46: System equations and telemeter SNR
The photoreceiver (photodetector+transimpedance amp.) detecting receiver optical power Pr has electronic noise to be added to optical and shot noise to obtain the total noise power Pn (as incident optical power on the photodiode)
In order to work with a given ratio (S/N)=Pr /Pn at the telemeter receiver, we must have:
remind
that we have
telemeter equivalent power
The received signal optical power is Pr (depending on Ps)


## Slide 47: Equivalent power vs. Leq and …
We observe that the telemeter equivalent power
is directly proportional to (S/N) and to Pn
inversely proportional to the receiver area (i.e. Dr2)
and directly proportional to Leq2
Fixing the other parameters, we can see on bilogarithmic scales different parallel lines (for different Pn levels) as increasing Peq with increasing Leq and we can identify some typical working regions for optical telemeters

## Slide 48: Power vs distance (equivalent)
CW telemeter Ps=0.1mW G=104 (s=10mrad)
Tmis=10ms-1s
B = 1/2Tmis = 100Hz-1Hz
Pn  "nW"
Pulsed telemeter Ep2mJ 10ns Ps,p=0.2MW G 0.5 (non-cooperative)
B  1/= 100MHz
Pn  "W"
equivalent distance L/(Tatm)0.5 (km)
equivalent power G Ps (W)
GPs  L2  equivalent power must be increased by two orders of magnitude for an increase of L by one order of magnitude
eq. opt. power
100 kW
1 W

## Slide 49: Noise at the receiver (of the telemeter)
3 "optical" noise contributions to noise power Pn:
- noise Pn,r associated to received signal (Pr)
- noise Pn,bg associated to background light (Pbg on the detector)
- noise Pn,el of photodetector and transimp. amp. (front-end)
Pn = Pn,s + Pn,bg + Pn,el
Ir=Pr is the “useful“ signal, Ibg=Pbg is the background and clearly Irec=Ir+Ibg (resp. =e/h)
Let’s evaluate the current noise irec on photodiode output Irec:
- shot noise on Ir  ir2 = 2eIrB  in,s
- shot noise on Ibg  ibg2 = 2eIbgB  in,bg
- electronic noise  iel2 = 2e"Iel,0"B  in,el
this noise is practically observed AFTER the photodiode but it is virtually “transferred" to its "input"
P optical power; I DC current; i AC current

## Slide 50: Noise at the receiver (of the telemeter)
the global variance, or power, of current noise (sum of variances of uncorrelated quantities) is:
irec2 = in,s2 + in,bg2 + in,el2 = 2eB ( Ir + Ibg + Iel,0 )
Dividing the two DC photocurrents and the noise equivalent current by the squared spectral responsivity (2) we get the optical power noise at the receiver:
Pn2 = ( 2h/) B ( Pr + Pbg + Pel,0 )
Let’s see some typical behaviors of electronic noise in,el (A/Hz1/2) for photoreceivers (photodiode+amp.), at different operating frequencies...
Starting from the 3 noise contributions:
- shot noise on Ir  ir2 = 2eIrB  in,s
- shot noise on Ibg  ibg2 = 2eIbgB  in,bg
- electronic noise  iel2 = 2eIel,0B  in,el
“equivalent” DC current producing a shot noise equal to the electronic noise transferred to the photodiode input
.../2

## Slide 51: Electronic noise for different photoreceivers
PD area A<0.5mm2 Capacity C<0.5pF
see (and “see again") the Book examples

## Slide 52: Evaluation of the background light (optical background power Pbg)
We start from the solar light spectrum (slide 45) and from the working conditions (AM, clouds, etc.): we get the scene spectral radiance Escene (W/m2m) that multiplied ("integrated") over the bandwidth  of the interference filter, gives the optical intensity of background light (“scene”):
Isc = Esc  (W/m2) scene “background" intensity
Optical power collected on the receiver is 1/ times the background intensity (Isc) times the scene diffusivity (sc) times the viewing solid angle (sc) [received intensity Ibg] finally multiplied by the receiver area (A=dr2/4):
Ibg = (1/)[ scIsc  sc(W/m2)
Pbg = [ sEsc dr2/4(W)
being = 2(NA)2 with NA=sin(Dr/2f ) Numerical Aperture
( in this slide "I" stays for optical intensity and not electric current )
sc=NA2

## Slide 53: Accuracy of the pulsed telemeter
In general, if not SNL, the background light and electronic noise contributions do increase the whole noise worsening the situation!
In a well-designed receiver (shot-noise limited, SNL) :
number of received photons (over a single pulse or as the sum or “average” over N pulses)
for SNL Pn2 = ( 2h/) B ( Pr + Pbg + Pel,0 )

## Slide 54: Accuracy of the CW sine-modulated telemeter
In analogy with the pulsed telemeter, now the term 1/2fm is equivalent to the duration  of the pulse: - pulsed telemeter: better working with short pulses (small ) - CW sine-modulated telemeter: better working with an high modulation frequency (high fm)
We would like to have a high fm (or high pulse repetition rate, allowing for "pulse averaging" in the pulsed case) but this will cause measurement ambiguity problems
Usually for Q-switch  10ns << (1/2fm)1s for a typical fm 200kHz and hence T,p<<T,CW-mod. (in the SNL case) but due to electronic noise Bp 1/ 100MHz >> BCW-mod.1/2Tmis 100Hz-1Hz
(SNL difficult when pulsed)

## Slide 55: Ambiguity in Time Of Flight telemeters
Working with a periodic signal (transmitted and hence also received repeatedly), we have an ambiguity problem in distinguishing targets at different distance that may return an optical signal with the same measurement information (time of flight or phase delay in the round-trip):
In order to avoid measurement ambiguity, we must have:
- pulsed telemeter:
Tmax=T(Lmax)  Trep  Trep  Tmax
- CW sin-mod telemeter:
max= (Lmax)=2fmTmax  2 fm 1/ Tmax
where Tmax is the “maximum Time Of Flight” corresponding to the maximum distance Lmax, said LNA, correctly measurable

## Slide 56: Ambiguity in Time Of Flight telemeters
When fmod is “low" or Trep is “high" (i.e. frep low) there is no ambiguity Pb. [but litlle averaging and poor SNR]
Pb.
amb.
Pb.
amb.
OK
OK

## Slide 57: Ambiguity in Time Of Flight telemeters
- pulsed telemeter:
Q-switched laser 10 ns frep=10Hz10kHz (repetition rate)
from Trep=Tmax we get LNA=(c/2)Trep=c/2frep=15000km15km
the problem arises only at large distances and/or for high repetition frequency of the pulse [it is useful repeating measurements of single pulses in order to increase the accuracy (“averaging")]
- CW sine-modulated telemeter:
diode laser with fm=10MHz10kHz (current modulated)
from fm=1/Tmax=1/(2LNA/c) we get LNA=(c/2)Tm=(c/2)(1/fm)=15m15km (100kHz1500m)
the problem arises already at medium-short distances
To achieve high accuracy we want high fm (“averaging") but to reach high distances we must keep fm low... combined use of 2 frequencies fm1 e fm2

## Slide 58: LIDAR
Light Identification Detection And Ranging
very similar to a telemeter, it is an instrument for measuring “at distance” the properties of a medium trough which the optical pulse undergoes transmission and backscattering

## Slide 59: LIDAR
Laser source with high peak power (Q-switched) at one or more suitable wavelengths to detect absorption and scattering from the investigated components within the medium (gas or particulate in the atmosphere, or pollutants or plankton/chlorophyll/seaweed in water, etc.).
backscattering signal (OTDR technique)

## Slide 60: LIDAR
From measured Time Of Flight T =2L/c we get the distance of the investigated target (  size of investigated volume);
from measured backscattered signal we get the composition (chemical/physical) of the investigated volume;
we obtain maps, also in fake colors, as a function of the telemeter elevation angle and distance