## Slide 1: “Optical Measurements” Master Degree in Engineering Automation-, Electronics-, Physics-, Telecommunication- Engineering
Optical Velocimeters Prof. Cesare Svelto Politecnico di Milano

## Slide 2: Summary
Measurement principles and application Doppler effect (on laser beams) Heterodyne method for velocimetry (laser Doppler)
Velocity measurements in fluids LDV (Laser Doppler Velocimetry) PIV (Particle Image Velocimetry)
Autovelox - optical barrier - tele-laser (time of flight and Doppler)

## Slide 3: Doppler effect (on laser beams)
The observed optical frequency (obs) is smaller than the one emitted by the laser () when the object moves farer [or obs>when object gets closer ]
v
LASER
OBJECT
Considering a velocity v << c, the Doppler shift
 = ( -obs) = (v/c ) << 
is much smaller then the optical frequency
[for =0.6 m (=500 THz), v=1 m/s  1.7 MHz,  /  3.310-93 ppb!]

## Slide 4: Heterodyne method for velocimetry
To detect f of a few MHz on the optical beam at 500THz we can not use a monochromator or OSA but much better (being f/f0=/<<1) to measure the “heterodyne” beat signal with a reference laser beam
 v
633 nm
Projection at cos() of v on the direction of the laser beam


f=vcos /c

## Slide 5: Laser Doppler Velocimetry (LDV)
LDV was invented in 1964 and is still today a great success of optical measurements, to contactless detect a wide range of velocities in moving fluids
The LDV techniques are used to measure velocity of fluids (liquids /gases) carrying diffusing (scattering) particles, naturally present or artificially “inseminated” in the fluid
The diffusion, or scattering, due to interaction of the e.m. field and the particle can be mainly of two types:
- Rayleigh ( r << ) s  r/4 f ( ) constant with the angle
- Mie ( r > ) s  cost. f ( ) max. for  =0 (forward scatt.)
The measurement signal can be seen as due to:
- fringe crossings  - Doppler effect - interferometric phase shift

## Slide 6: LDV: measurement set-up
The two collimated beams impinge off-axis on the lens and are focused at distance f from the lens in an interference region
Two-beams interferometer
f
example: R=0.5cm and f=250mm   20mrad=1.15°1°
v

## Slide 7: LDV: interference fringes
Φ(OA)=[Φ2-Φ1](O)-[Φ2-Φ1](A)=2 fringe spacing D dark/dark
From O to A: Φ2=Φ2(OC)+Φ2(CA) and Φ1=Φ1(OB)+Φ1(BA) Φ2=(0+k2CA)=+(2/)Dsin and Φ1=(0-k1BA)=-(2/)Dsin
collimated beams  wavefronts approx. plane with width ±w0
the interaction zone is wide X=2w0cos Y=2w0sin
zoom
Φ(OA)=Φ2-Φ1=2(2/)Dsin =2
x
y
+k2Dsin
-k1Dsin
Light peaks repeated at distance D (  a v)
D sin = / 2

## Slide 8: LDV: relation velocityfrequency
The optical beam profile, crossed by particles, is Gaussian and hence diffused light intensity profile varies with position. The frequency of alternating light-dark-light depends on the fringe distance and particle/fluid velocity fD = 1/TD  v
Thickness of crossing zone changes with position of crossing line (in the lit zone) but light-light distance remains constantly D in orthogonal direction to the interference zone.
On a time axis the distance TD between light peaks depends on velocity v
TD repetition period of light peaks
TD  1 / v
e.g. at tube center
e.g. at tube sides

## Slide 9: LDV: signal period and frequency
TD = D / v period of diffused light signal (light-dark-light)
v
MEASURE SENSITIVITY: Sf  v=f/v =2sin / (Hz/ms-1)


Measure of fD: 1) counter; 2) electron. AS; 3) correlation
=2w0sin

## Slide 10: LDV: schemes (angle_scatt./back_scatt.)
D

## Slide 11: LDV: photos of 3D LDVs

## Slide 12: LDV: practical example
.

## Slide 13: LDV: properties
for the Doppler analysis of LDV signal see the Text Book (Prof. Donati)
2
2

## Slide 14: PIV (only measurement "principle")
The velocity measurement of the particles in the fluid is done “lighting” the investigation zone, with laser light (or with fast light flashes and using a multi-exposure slow camera)
Images of the particles as a function of time are detected with a fast CCD camera, from which one can reconstruct the entire spatial profile (field) of velocities: vi=li/t

## Slide 15: Autovelox with optical barrier (e.g. 104 C2)
Detection with NIR laser (Class 1)
No interception/countermeasures
PLATE imaging by photo/video
optical barrier
D = 0.5 m
D
T1
T2
v=D/(T2-T1)=D/21
v
E.g. for v=150 km/h 21=12 ms
2110 sv=-D/(21)2  210.1 km/h
barrier
photo

## Slide 16: Autovelox with optical barrier (e.g. 104 C2)
The target is hit by the laser and retro-diffused light is detected
v21,ON=D/21,ON
v21,OFF=D/21,OFF
D
T2,OFF
T1,ON
T1,OFF
T2,ON
21,OFF
21,ON
Measurement independent from vehicle profile and double-detection (v21,IN  v21,OFF within 1 km/h) allows discarding fake readings and meas. errors
t

## Slide 17: Autovelox with optical barrier (e.g. 104 C2)
Co-planarity (Orizz.= = 0) of the optical barrier with the road is important and instrument calibration is mandatory by law every year
The horizontal instrument measures
v = v21 = D/(T2-T1) = D/21
but if inclined by  the measure is
21*= (t2-t1) = d/v < 21 and hence
v* = D/21* = vD/d = v /cos > v
the velocity can be “overestimated”
D
T1
T2
v
d = D cos < D
d
t1
t2
If well aligned and calibrated, the instrument can reach accuracy levels well below 1% that – “poor us!” – are more than adequate for the measurement, given with a “tolerance” of 5%
A misalignment barrier-to-road of 10° gives a measurement error of 1.5% (in excess!), corresponding to +2.3 km/h at 150 km/h
horizontal vs. inclined

## Slide 18: Tele-laser (Doppler velocimeter) “???”
v
LASER
Given the high value of Doppler, TDoppler <1 s, repeated vj measurements “could” be averaged in a short time, reducing measurement uncertainty
Tobs
Tobs
T
T
t
t
By beat-note analysis we “could” detect a the Doppler shift
 Doppler = ( -obs) = (v/c )  = ( 1/ )  v
[for =1 m (=300 THz), v = 108 km/h = 3 m/s  = 3 MHz]
[for =1 m (=300 THz), v = 36 km/h = 1 m/s  = 1 MHz]
[for =1 m (=300 THz), v = 180 km/h = 5 m/s  = 5 MHz]

## Slide 19: Tele-laser “pistol” (TOF telemeter)
Technical specs.:
Tmeas=0.4 s
L-Range=610 m
v-Range=±320 km/h
=904 nm
div=3 mrad
laser class 1
u(L)=15 cm
u(v)=2 km/h

## Slide 20: Tele-laser (TOF telemeter )
Trep=TNA=2LNA/c  4 s (frep=250 kHz) with LmaxLNA=600 m
v = (L2-L1)/Trep = c/2  (T2-T1)/Trep
v
LASER
L1 = c/2  T1
v
LASER
L2 = c/2 T2
Given the high value of frep, repeated TOF measurements can be averaged in a short time (Tave=10 ms and Tmeas=0.4 s: average of 40 readings of TOF for Li meas. and 39 readings of vj for vave@400ms) reducing measurement uncertainty
T  0.4 s
L  5.6/20 m @ 50/180 km/h