## Slide 1
<number>/33
LASER Sources: Properties and Applications prof. Cesare Svelto Politecnico di Milano
“Optical Measurements” Master Degree in Engineering Automation-, Electronics-, Physics-, Telecommunication- Engineering
Notes: 07/29/26
<number>
Buongiorno a tutti,
sono Cesare Svelto
del Politecnico di Milano.
Questa mattina vi parlerò delle sorgenti laser in continua e delle pricipali misure per la loro caratterizzazione.
Descriveremo la struttura dei laser a stato solido e dei laser a semoconduttore (diodi laser)
per la caratterizzazione di sorgenti laser in continua e dei campioni ottici di frequenza.
La prima parte del mio intervento sarà seguita da una lezione del Prof. Elio Bava sui modelli descrittivi dell’instabilità di frequenza e sulle relative tecniche di misura.
Nella seconda metà della mia presentazione descriverò, dal punto di vista sperimentale, alcuni metodi ed esperienze di stabilizzazione e la realizzazione di campioni ottici di frequenza.

## Slide 2: Main Properties of LASER Sources
<number>/33
Properties of LASERS
  Monochromaticity (laser ~10-610-9spectral lamp)
  Brightness B=P/A (Blaser=105 108 W/m2sr >> BSUN)
  Stability in amplitude (P/P~10-5) and frequency ( / ~10-15)
  Ultrashort pulses (~10-15 s), high peak power (~1015 W)
  Size (from ~1 m up to a few km)
  Propagation: in free space or in optical fibers
  Commercialization: compact and low costs and low power
Notes: 07/29/26
<number>

## Slide 3: Physical properties and Applications of LASER Sources
<number>/33
Typical properties of LASERs
  Spatial quality of the beam SPATIAL COHERENCE
  Spectral quality ("monochromaticity") TEMPORAL COHERENCE
  Wavelength “COLOR”
  Optical Power or pulse energy
  “SOP” State Of Polarization
Applications of LASERs
  Experiments of Physics, Metrology, Telemetry, Interferometry, Optical Communications, industrial processing (marking, cutting, welding, quenching), printers, scanners, bar-code readers, pointers, alignment, Optical References, optical measurements and optoelectronic sensors
Notes: 07/29/26
<number>

## Slide 4: Properties of LASER beams (TRANSVERSE PROFILE and fundamental mode TEM00)
<number>/33
minimum size w0 in z=0 is the beam waist
standard size w>w0 in z≠0 is the spot size (spot dimension)
Optical intensity profile [W/m2] in a plane (x-y) transverse to the propagation direction (z): depends on the spatial mode and its “width”
x
y
Fundamental LASER mode TEM00 is symmetric in both directions x and y with a 2D GAUSSIAN profile, both for electric field and intensity, with a spot size or “width” w0 at beam waist (37%E0 o 13.5%I0) [w0w for z0]
Notes: 07/29/26
<number>

## Slide 5: Properties of LASER beams (TRANSVERSE PROFILE and “width” of the spot – spot size)
<number>/33
Within a circle of radius r = w0 we find 86.5% of the whole power P0 of the laser beam. We call w0 the beam waist or also w the beam (standard) spot size of the laser beam (at 1/e2 of the peak intensity)
The optical power P is the integral of the intensity I over a collecting surface S (e.g. circle of radius r)
power collected within a circle of radius r P0 is the whole power of the beam (with r “big” r )
if e-2=13.5%
1-e-2=86.5%
86.5%P0
w0
Notes: 07/29/26
<number>

## Slide 6: Properties of LASER beams (TRANSVERSE PROFILE and integration over a circle)
<number>/33
For r =( 0.5, 1, 2 )  w0 we get P=( 40%, 86.5%, 99.97% )  P0
Power P (normalized to P0) as the integral of the intensity I over a circle of radius r (normalized to w0)
Notes: 07/29/26
<number>

## Slide 7: Properties of LASER beams (TRANSVERSE PROFILE and higher order modes TEMlm)
<number>/33
More in general the transverse profile of the electric field (transverse mode) can be described by the product of two (Hermite) polynomials, in directions x and y, and a 2D Gaussian curve with radial symmetry. Indexes and hence degree of the two polynomials set the order of the mode: TEMlm
Hermite polynomials
of order 0, 1, 2, ..., 5
Zero order = unitary constant
Odd/even order corresponds to odd/even symmetry i-th order  i “zeros” on the axis
Notes: 07/29/26
<number>

## Slide 8
<number>/33
For l=0 and m=0, from H01 we get TEM00 with Gaussian (2D) profile
The order of a polynomial tells us how many zeros cut the Gaussian curve along the corresponding axis
Also for higher order modes we define a spot size equal to the radius w0,lm of the circle containing 86.5% of the whole optical power of the mode
Increasing the mode order, the spot size increases and the divergence as well!!! (spatial beam quality gets worse compared to TEM00)
then w0w(z)…
Properties of LASER beams (TRANSVERSE PROFILE and first higher order modes TEMlm)
Notes: 07/29/26
<number>

## Slide 9: Free-space propagation
<number>/33
“Spot broadening” (divergence)… w=w(z)
"w grows" during propagation of the beam/mode along z axis
w
z
0
w0
We call Raileigh distance/range
w0
zR
z<zR
z>zR
when z=zR, the beam is wider 40% more with respect to its minimum dimension (w  1.4 w0)
w  w0 w z
beam “radius” or spot size changes with propagation
Notes: 07/29/26
<number>

## Slide 10: Near/far field and beam divergence
<number>/33
e.g. for a laser beam
with =1 m , w0=1 cm
we have =30  rad!!!
 “small” high
directivity
w
z
0
w0
w0
zR
divergence angle

We have two asymptotic work regions: near field when z<<zR and the “beam is collimated” far field when z>>zR and the “beam is divergent" (linearly)
In a multimode beam with beam waist w0 we have a divergence MM>DL=/w0 and can define a factor M2=(MM /DL)>1 stating the spatial quality of the beam
laser beam
diffraction-limited
(minimum divergence)
Notes: 07/29/26
<number>

## Slide 11: Guided propagation (optical fiber)
<number>/33
Guided mode HE11
Low attenuation  < 0.2 dB/km at 1.55 m ( = -4.5%/km )

Numerical Aperture
 “piccolo” alta
direzionalità
z
n2 cladding
n1 core
l
c
a
optical fiber
n1>n2
Problems:
Chromatic Dispersion [ps/(nmkm)]
Polarization Mode Dispersion [ps/km-1/2]
SM fiber
n1.45
n510-3
core=9 m
clad=125 m
For PMD “dispersion” is a differential delay as a st.dev. from a variance [ps2/km] after a propagation length L [km]
Notes: 07/29/26
<number>

## Slide 12: Properties of LASER beams (AMPLITUDE NOISE)
<number>/33
Electric field varying in time with amplitude fluctuations
with a(t) << 1
Need for stabilization systems (passive/active)
( x = P/Pth is the above-threshold )
A small-perturbation analysis of the laser system (in response to small variations of the pump rate or of the cavity losses) reveals the phenomenon of relaxation oscillations
  oscillation frequency
  (exponential) decay time
Notes: 07/29/26
<number>

## Slide 13: Properties of LASER beams (FREQUENCY NOISE)
<number>/33
Electric field varying in time with frequency fluctuations
 (t) = [1/(2)] dtot/dt = 0+(1/2) d/dt = 0+
with  << 0
Need for stabilization systems (passive/active)
From the equation of the resonator modes frequencies:
Strong dependence of the laser frequency on L
  e.g. for an Nd:YAG LASER (=1.064 m,  300 THz)
  with L=30 cm if L=-1 m, one has  =1 GHz!!! (1nm1MHz)
“instantaneous” frequency or
average frequency?
Notes: 07/29/26
<number>

## Slide 14: Optical Power (DEFINITIONS and MEASUREMENT METHODS)
<number>/33
E=E0exp(-j0t) Electric field [V/m]
Laser
calibrated detector
Voltage output
Vu
calibrated attenuators
P
P
2
1
3
Vu =P
P = Power [W]
I0 = Intensity [W/m2]
0 = (0/0)1/2 = 377 
characteristic impedance of the vacuum
sensitivity
Notes: 07/29/26
<number>

## Slide 15: Photo-voltaic /-conductive Detectors
<number>/33
(Si, HgCdTe, Ge, GaAs, GaAsP, InGaAs) 0.1m    10m
(A/W)
 [ m]
0.3 0.5 0.7 0.9 1.1 1.3
0.5 0.1 0.001
 c
Si  0.8 photodiode
Responsivity
h>Eg
Quantum efficiency
photon flux ( #phot./s = Nph/T )





h
e

h
P
t
e
N
e
i





energy
gap
mat. abs.

MICRO
MACRO


h
e
c

Notes: 07/29/26
<number>

## Slide 16: Typical Si photodiode responsivity
<number>/33
0
200
400
600
800
1000
1200
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
Wavelength (nm)
Si Photodiode
g
Responsivity (A/W)
Ideal Photodiode
QE = 100% (

= 1)
(500 nm)=0.25/0.40=0.623 (700 nm)=0.425/0.55=0.77
Notes: 07/29/26
<number>

## Slide 17: Photodiodes (output current)
<number>/33
When an optical beam (uniform) with intensity I (W/m2) impinges on a photo detector with surface S (m2), the collected optical power is
P = IS (W)
If the photo detector is a photodiode, the output is a current signal directly proportion to the optical power impinging on the photo detector:
i =  P (A)
where the conversion factor  between photocurrent I and detected optical power P is the sensitivity (“responsivity”)  (A/W) of the material by which the photodiode is made (Si0.3-0.4 A/W in the VIS and InGaAs0.8 A/W in the NIR)
Notes: 07/29/26
<number>

## Slide 18: Photodetectors (voltage output)
<number>/33
The photodiode current is typically amplified by a resistance gain (transimpedance), let’s say with gain Giv (V/A) = R (), in order to produce an output voltage
v = Giv i = Giv   P (V)
Among the time fluctuations of the electric field in the optical signal, we can observe/measure in the voltage signal only those fluctuations whose frequencies are in the passband of the photodetector ( photodiode + trans.amp. )
Thus the voltage is directly proportional to the optical power (or intensity) on the detector, i.e. the squared amplitude of the electric field (at optical frequency) reaching the detector:
v  P  I  EE* =E2
Notes: 07/29/26
<number>

## Slide 19: Direct optical detection
<number>/33
Let us consider the LASER beam electric field
E(t)=E0[1+a(t)]exp[-j(20t+(t))]
amplitude mod. (eventually)
phase&freq. mod. (eventually)
amplitude (V/m)
frequency (THz)
The “direct” photodetected voltage is
v(t)  EE* = (E0)2 [1+a(t)]2  P(t)=P0 mod(t)
All the information about phase&frequency variations of the optical signal gets lost, while the electric signal shows a sensitivity to variations (attenuation) of the optical power
depend on measurement signal
Notes: 07/29/26
<number>

## Slide 20: Beating (heterodyne) of two optical signals
<number>/33
Take two laser beams impinging on the photodetector and, for the sake of simplicity, neglect amplitude fluctuations
EL(t)=EL0exp[-j(2Lt)]
for simplicity we choose L=0
LOCAL OSCILLATOR
Considering two electric fields, linearly-polarized (in the same direction), the resulting field by the superposition in space (hence “sum”) of the two fields, so the total field, is
E(t)=ER(t)+EL(t)
RECEIVED SIGNAL
ER(t)=ER0[1+a(t)]exp[-j(20t+(t))]
amplitude mod.
phase/freq. mod.
Notes: 07/29/26
<number>

## Slide 21: Coherent detection (heterodyne)
<number>/33
The corresponding optical power is
Changing the phase (t) the power oscillates between Pmax=[(PR)1/2+(PL)1/2]2 e Pmin=  abs[(PR)1/2-(PL)1/2] 2 Practically we sum the fields and hence P1/2
In the particular case where ER0= EL0= E0 and hence PR=PL=P0 we obtain ”complete interference between the two signals”: Pmax = 4P0 e Pmin = 0
and depends on the phase  of the detected optical signal
interference
beat note frequency
with 2 BS at 50% we get PR=PL=P0=Plaser/4
Notes: 07/29/26
<number>

## Slide 22: Interference for different ratios PR/PL
<number>/33
PR / PL
Note that with just 1% of interfering power it is possible to observe a fringe visibility V=(PM-Pm)/(PM+Pm)=(1-0.67)/(1+0.67)20%
V20%
V=100%
V2%
Phase (rad)
Notes: 07/29/26
<number>

## Slide 23: Measurements with coherent detection
<number>/33
The variable optical power, and hence photodetected voltage, is a function of the phase (t) of the detected signal ER(t): we get phase sensitivity
A measurand M (physical parameter of interest) changing the phase (t) or the frequency  =(1/2)(d /dt) of the detected signal can be coherently detected and measured observing variations of phase/frequency of the beat signal at the intermediate (electronic) frequency IF=(R - L)=(0 - L), easily falling in a radio-frequency band (tens or hundreds of megahertz) or even at lower electrical frequencies
Performing coherent detection and observing the phase of the intermediate frequency signal, we can also obtain a measurement proportional to sin[(t)] that, for “small variations” of the measurand ( dM/dt such as d /dt<<1 ), is directly proportional to (t) and hence to variations of M (in this case we say that the interferometer is “in quadrature”)
Notes: 07/29/26
<number>

## Slide 24: Example of beat measurement
<number>/33
The photosignal V oscillates at about the frequency fAOM still depending, in its exact electrical phase/frequency, on the optical phase/frequency changes driven by the measurand
V ERIV2 = (E0)2 + (E0)2 + 2(E0)2 cos[ 2fAOMt +(t) ]
EM(t)=E0exp[-j(20t+(t))]
M
AOM
LASER
MEASURAND changes 0 or 
PD
M
BS

EL(t)=E0exp[-j(2(0+fAOM)t)]
E0exp[-j(20t)]
fAOM
V
Notes: 07/29/26
<number>

## Slide 25: LASER safety diagram
<number>/33
CL 1: secure CL 2: secure (visible light) CL 3: dangerous CL 4: very dangerous
Notes: 07/29/26
<number>

## Slide 26: LASER safety (1/2)
<number>/33
Class 1
a) Use without prescriptions
Class 2 [[only for visible ]] (direct vision practically safe)
a) Avoid protracted vision of direct beam (shutting-eye reflex!)
b) Do not aim the beam directly at people
Class 3A (direct vision little dangerous)
a) Avoid use of optical focusing systems e.g. ocular, theodolite
b) Post a LASER advice note
c) Laser alignment by mechanical or electronics means
d) Terminate the beam in an zone external to the working area or enclose the working area
e) Chose an height of the laser beam well above the eye-sight
f) Avoid directing the laser beam onto reflecting surfaces
g) Store the portable laser, when not used, out of reach from unauthorized persons
Notes: 07/29/26
<number>

## Slide 27: Laser safety (2/2)
<number>/33
Class 3B (direct vision always dangerous; diffused light vision potentially dangerous)
Can cause damage to unprotected eye. Same prescriptions as for class 3A and
a) Use only in areas controlled by instructed operators
b) Absolutely avoid direct reflections
c) Terminate the beam on absorbing material designed for heat dissipation
d) Were eye-protection (laser-safety goggles!)
Class 4 (direct vision extremely dangerous; diffused light vision dangerous)
Causes damage to the eye with direct or reflected or diffused beam. Potential danger of skin burning and fire onsets. Same prescriptions as for class 3B and
a) Beam paths protected by physical enclosures that can stop the beam
b) During use, only technical personnel can be present and must be protected by proper eye-protecting-goggles and wearing special protecting dresses
c) To avoid the presence of personnel it would be preferable a remote control of the laser devices and apparatuses
d) Use non-flat metallic targets properly cooled e.g. absorbing cones
e) To avoid undesirable reflections in the invisible part of the spectrum (for FIR light) the beam path and the impact area should be enclosed inside an opaque material to the laser wavelength
Notes: 07/29/26
<number>

## Slide 28: LASER protections
<number>/33
Eye protections
A prescribed eye protection must be used (LASER goggles: OD=log10[1/T] if T=10-x then OD=x) to ensure adequate protection against specific laser wavelengths in all dangerous areas where class 3 and class 4 lasers are in use.
Protective dresses
To be used where operating personnel is exposed to radiation levels above the MPE (Maximum Permitted Exposure) for the skin (class 4 lasers are a potential risk of fire onset and the protecting dresses must be fabricated with proper anti-fire materials).
Formation
Security classes 3 and 4 lasers can be a danger not only for the operator bu also for other people, even at large distance. The personnel operating these lasers must have adequate preparation in order to minimize the professional risks.
Medical surveillance
Oculistic exams, before work start and during work period, should be performed on personnel operating with lasers in the laser security classes 3 and 4.
Notes: 07/29/26
<number>

## Slide 29: LASER safety diagram
<number>/33
Notes: 07/29/26
<number>

## Slide 30: Industrial LASER applications
<number>/33
Material processing
Drilling, cutting, soldering, thermal hardening, etc.
Industrial measurements, civil and envirromental
Industrial compartment: interferometers for dimensional laser metrology, wire diameter measurements, granulometers, roughness meters, deformation fields detectors.
Civil compartment: alignment laser systems, laser levels, topographic telemeters and geodimeters.
Environmental compart: LIDAR for pollutant remote monitoring.
Presentation compartment: lasers for holograms visualization, laser pointers for conferences, didactical usage laser systems.
Light show compartment: laser for special effects in discotheques, exhibitions, open-air shows and similar.
Durable goods compartment: laser bar-code readers, compact disk players, laser printers and similar.
Notes: 07/29/26
<number>

## Slide 31: Applications of LASERs for TLC, Medicine and Basic Research
<number>/33
Telecommunications and optical fibers
Semiconductor lasers for usage, with optical fibers, in data transmission and processing and networking
Medical fields
Laser applications in Ophthalmology
Clinical applications of lasers in General Surgery
Clinical applications in Surgery with operatory microscopy
Clinical applications in Endoscopic Surgery
Research laboratories and experiments
Nonlinear optics
Spectroscopy (linear and nonlinear)
Interaction of radiation with mattera
Ultrafast optical pulses
Precision Measurements
Notes: 07/29/26
<number>

## Slide 32: Conclusions
<number>/33
Physical principles and devices for LASER action
Solid-state and semiconductor laser structures
Principal properties of lasers
Free-space and guided propagation
Properties of laser beams (profile, noise amp. / freq.)
Optical power and photodetection
Laser safety and applications
LASER “bright solution in search for a problem”
laser instrumentation: now widely used in research, technology , R&D, production, optical measurements
Notes: 07/29/26
<number>
A conclusione,
possiamo dire che abbiamo descritto i principi fisici su cui si basa l’azione laser e i dispositivi che consento di costruire una sorgente laser in continua.
Quindi, abbiamo visto le principali proprietà dei fasci laser e le misure: di potenza ottica, con gli associati rivelatori, di profilo trasversale, della lunghezza d’onda e dello spettro ottico.
Sono poi stati descritti alcuni metodi e sistemi per la stabilizzazione, in ampiezza e frequenza, delle sorgenti laser .
Da ultimo, abbiamo riportato alcuni esempi di campioni di frequenza ottica.
Se dopo l’invenzione del laser e le sue prime realizzazioni si usava dire che: “*”,
oggi possiamo dire che gli strumenti laser trovano vasta applicazione in diversi campi della ricerca scientifica, nel settore tecnologico-produttivo e per le misure opto-elettroniche.

## Slide 33: Bibliography
<number>/33
J. M. Vaughan, The Fabry Perot Interferometer, Hilger, Bristol, 1989
A. Yariv, Quantum Electronics, 3th ed., Wiley, New York, 1989
A. E. Siegman, Lasers, Oxford University, Cambridge, 1986
O. Svelto, Principles of Lasers, 5th ed., Plenum, New York, 2010 (from which some figures of this Chapter are reproduced)
W. Koechner, Solid-State Laser Engineering, 6th ed., Springer, Berlin, 2006
Notes: 07/29/26
<number>
Riportiamo, infine, i riferimenti ad alcuni testi scientifici che possono essere usati per approfondimenti sugli argomenti presentati.
E’ stato un privilegio e un piacere insegnare in questa Scuola.
Gazie per la vostra attenzione.