## Slide 1: Politecnico di Milano Optical Measurements ”LASER INTERFEROMETRY”
Dr. Eng. Enrico Maria Randone, Ph.D.
Dipartimento di Elettronica - Università di Pavia
Tel. 0382 98 5224
e-mail: enrico.randone@unipv.it
It is acknowledged the origin of some figures, photos and texts
as didactic material originally produced by Prof. Silvano Donati (Università di Pavia)
and/or Dr. Eng. Guido Giuliani (Università di Pavia)

## Slide 2: Working Principle
Iph =  Em + Er2 = Em exp jm +Er exp jr2
Iph = [ Em2 + Er2 + 2EmEr Re{ exp j(m-r) } ] = Im+ Ir + 2(ImIr)½cos(m-r)
r=ksr, m=ksm  m – r = k(sm-sr) = 2π(sm-sr) / λ
What is the value of sm-sr that gives a phase difference m – r = 2π? When m – r = 2π, an interferometric fringe is seen on Iph
This setup is equivalent to a HOMODYNE COERENT DETECTION SCHEME and for this reason it always performs at the QUANTUM-LIMIT REGIME OF DETECTION: Signal to Noise Ratio depends only on the SIGNAL level
Single Mode
LASER
PHOTODIODE
REFERENCE PATH - Er
MEASUREMENT
PATH - Em

m
r

/2

/2


Iph
PHOTO-CURRENT Iph
Em
sm
sr
MOVING
TARGET

## Slide 3: Simple Principle But MANY Applications
V
I
B
R
A
T
I
O
N
A
n
a
l
y
z
e
r
s
s
c
i
e
n
t
i
f
i
c
u
s
e
s
t
e
c
h
n
i
c
a
l
u
s
e
s
s

1
k
m
s

1
O
O
m
s

1
m
s

<
1
c
m
I
N
T
E
R
F
E
R
O
M
E
T
E
R
S
f
o
r
M
E
C
H
A
N
I
C
A
L
M
E
T
R
O
L
O
G
Y
D
O
P
P
L
E
R
V
E
L
O
C
I
M
E
T
E
R
S
f
o
r
A
N
E
M
O
M
E
T
R
Y
E
S
P
I
(
S
P
E
C
K
L
E
P
A
T
T
E
R
N
)
R
L
G
a
n
d
F
O
G
G
Y
R
O
S
C
O
P
E
S
a
v
i
o
n
i
c
s
i
n
d
u
s
t
r
i
a
l
u
s
e
s
S
P
A
C
E
T
E
L
E
M
E
T
R
Y
o
f
G
E
O
D
E
T
I
C
S
A
T
E
L
L
I
T
E
S
E
A
R
T
H
T
I
D
E
S
S
E
N
S
I
N
G
L
A
R
G
E
S
T
R
U
C
T
V
I
B
R
O
M
E
T
R
Y
M
E
T
R
O
L
O
G
Y
o
f
L
E
N
G
T
H
(
a
n
d
d
e
r
i
v
e
d
q
u
a
n
t
i
t
i
e
s
)
B
I
O
L
O
G
I
C
A
L
M
O
T
I
L
I
T
Y
S
E
N
S
I
N
G
A
C
O
U
S
T
I
C
E
M
I
S
S
I
O
N
a
n
d
S
A
W
S
E
N
S
I
N
G
G
E
O
D
E
T
I
C
G
R
A
V
I
M
E
T
R
Y
G
R
A
V
I
T
A
T
I
O
N
A
L
A
N
T
E
N
N
A
S
O
P
T
I
C
A
L
F
I
B
E
R
S
E
N
S
O
R
S
O
P
T
I
C
S
E
L
E
C
T
R
O
N
I
C
S
W
A
V
E
a
n
d
F
I
E
L
D
S
T
E
C
H
N
O
L
O
G
Y
M
E
A
S
U
R
.
S
C
I
E
N
C
E
LASER
INTERFEROMETRY

## Slide 4: Classical Interferometric Setup
PD
LASER
Fixed
Mirror
50/50 Beam Splitter (BS)
Mobile
Mirror
PD 1
LASER
PD 2
Mesurand
LASER
PD
Mesurand
Michelson
Mach-Zehnder
Sagnac
Fixed
Mirror
Fixed
Mirror
Fixed
Mirrors
Fixed
Mirror
BS
BS
BS

## Slide 5: Michelson Interferometer (I)
Iph = Im + Ir + 2(ImIr)½cos(2k(sm - sr)) = I0[1 + cos(2k(sm - sr))]
I0 = 2Im = 2Ir = ½PL, where  is the spectral responsivity of the PD
An interferometric fringe, or a phase difference 2k(sm - sr) = 2π, is found in Iph when the target moves of λ/2 = 316.4 nm
Laser He-Ne
(PL ~ 1mW)
λ = 632.8nm
Iph
Reference/Fixed Mirror (R = 100%)
Measuring Mirror/
Moving Target (R = 100%)
Beam Splitter
50/50
PD (σ = 0.5 A/W)
Sm
Sr

## Slide 6: Michelson Interferometer (II)
http://www.youtube.com/watch?v=87pPoGuLSuw

## Slide 7: Michelson Interferometer (III)
Simple digital approach for sm-sr measurement:
  Interferometric fringes count  Resolution Δs = λ/2
  Can we easily double the resolution?
  The idea works fine for target displacement of more than Δs!!
Laser He-Ne
(PL ~ 1mW)
λ = 632.8nm
Iph
Reference/Fixed Mirror (R = 100%)
Measuring Mirror/
Moving Target (R = 100%)
Beam Splitter
50/50
PD (σ = 0.5 A/W)
Sm
Sr

## Slide 8: Michelson Interferometer (IV)
Michelson Interferometer issues:
  The Laser suffers from back reflections into the optical cavity
  The alignment of the mirrors and the positioning of the beam splitter are very critical
Laser He-Ne
(PL ~ 1mW)
λ = 632.8nm
Iph
Reference/Fixed Mirror (R = 100%)
Measuring Mirror/
Moving Target (R = 100%)
Beam Splitter
50/50
PD (σ = 0.5 A/W)
Sm
Sr

## Slide 9: Twyman-Green Interferometer
With this new setup all the issues of the Michelson interferometer are solved:
  Absence of back reflections into the laser cavity
  Alignment of the Corner Cubes and positioning of the CBS is not critical and much easier to achieve
Reference/Fixed
Corner Cube
Measuring/Moving
Corner Cube
Iph
Sr
Sm
Photodiode
Laser He-Ne (~1mW)
λ = 632.8nm
Iph aux
Photodiode aux
CBS
(Cube Beam Splitter)

## Slide 10: Ambiguity of the cosine signal (I)
sm(t)
Iph
t
An issue arises when we need to measure also the direction of the moving target because the cosine is an even function of 2k(sm-sr)
Iph ≈ 1 + cos[2k(sm-sr)]
Iph aus ≈ 1 - cos[2k(sm-sr)]
We can’t solve this issue with the simple setups discussed until now

## Slide 11: Ambiguity of the cosine signal (II)
We have two solutions:
The DOUBLE-BEAM interferometer
The DOUBLE-FREQUENCY interferometer
sm(t)
Iph
t
An issue arises when we need to measure also the direction of the moving target because the cosine is an even function of 2k(sm-sr)
Iph ≈ 1 + cos[2k(sm-sr)]
Iph aus ≈ 1 - cos[2k(sm-sr)]
We can’t solve this issue with the simple setups discussed until now

## Slide 12: Double-Beam Interferometer (I)
Iph2
Sr
Sm
Laser He-Ne
x
y
45°
Laser Linearly Polarized
Iph1
Photodiode 1
Photodiode 2
Pol. 90°
Pol. 0°
λ/8 waveplate:
fast or slow axis aligned at 0° or 90°
CBS
The basic idea is to double the interferometer to obtain two signals with a phase difference of 90°: a cosine and a sine waves
Iph1 = Im + Ir+ 2(ImIr)½cos(2k(sm -sr)) = I0[1+cos(2k(sm-sr))]
Iph2 = Im + Ir+ 2(ImIr)½cos(2k(sm + /8 - sr )) = I0[1-sin 2k(sm-sr))]
I0 = 2Im = 2Ir = ¼PL
Reference/Fixed
Corner Cube
Measuring/Moving
Corner Cube

## Slide 13: Double-Beam Interferometer (II)
s (t)
m
cos 2ks
sin 2ks
I
0
threshold of
discriminators
t
A
c
A
s
S
s
S
c
t
Signals Analysis:
  sine and cosine signals are squared to obtain As and Ac signals
  The same operation is done on the derivatives of sine and cosine signals, and we get the slope squared signals Ss and Sc

## Slide 14: Double-Beam Interferometer (III)
s (t)
m
cos 2ks
sin 2ks
I
0
threshold of
discriminators
t
A
c
A
s
S
s
S
c
t
1
2
3
4
5
6
7
8
9
10
 | Ac | Ss | As | Sc
1 | 0 | 1 | 0 | 0
2 | 0 | 1 | 1 | 1
3 | 1 | 0 | 1 | 1
4 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 0
 | Ac | Ss | As | Sc
6 | 0 | 0 | 1 | 0
7 | 0 | 0 | 0 | 1
8 | 1 | 1 | 0 | 1
9 | 1 | 1 | 1 | 0
10 | 0 | 0 | 1 | 0
Signals Analysis:
  sine and cosine signals are squared to obtain As and Ac signals
  The same operation is done on the derivatives of sine and cosine signals, and we get the slope squared signals Ss and Sc

## Slide 15: Double-Beam Interferometer (IV)
s (t)
m
cos 2ks
sin 2ks
I
0
threshold of
discriminators
A
c
A
s
Counting Pulses (CNT)
Up/Down Logic Function
S
s
S
c
t
t
 | Ac | Ss | As | Sc
1 | 0 | 1 | 0 | 0
2 | 0 | 1 | 1 | 1
3 | 1 | 0 | 1 | 1
4 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 0
 | Ac | Ss | As | Sc
6 | 0 | 0 | 1 | 0
7 | 0 | 0 | 0 | 1
8 | 1 | 1 | 0 | 1
9 | 1 | 1 | 1 | 0
10 | 0 | 0 | 1 | 0
Signals Analysis:
  sine and cosine signals are squared to obtain As and Ac signals
  The same operation is done on the derivatives of sine and cosine signals, and we get the slope squared signals Ss and Sc

## Slide 16: Double-Beam Interferometer (V)
Each pulse is obtained for a displacement of the moving target equal to /8 = 0.079 m (instead of /2 or /4 as mentioned some slide ago…)
The logic functions U gives the correct sign of the target displacement: “UP” when U=1, “DOWN” when U=0
The UP-DOWN counter stores the information on target displacement in digital units equal to /8
U
PC + DAQ
or
Digital AdHoc
Circuit (PIC)
ex-or
or
A
s
S
c
A
c
S
s
Counting
Pulses

## Slide 17: Double-Beam Interferometer (VI)
This interferometer has been extensively used since its invention, however it is not perfect and has these issues:
Bandwith: can I work in DC or at very low frequency? Is this a baseband measure?
Can we measure target displacement with high velocities or does an upper limit exist?
The measure is obtained in an incremental way, so that an accidental interruption of the laser beam cause an error on it…
EMI are unavoidable when we work in baseband and can cause spurious count…
Environmental vibration can cause spurious count…
The value I0 used for the comparator is critical…
How can we solve these issues?

## Slide 18: Double-Frequency Interferometer (I)
This interferometer uses a Ne-Ne Zeeman laser that emits on two longitudinal mode, f1 and f2, circularly and orthogonally polarized. This way of emission is obtained thanks to a magnetic field B longitudinally applied to the laser cavity
On the measuring photodiode PDm the optical phase 2k(sm-sr) appears as a phase modulation around the carrier frequency, equal to |f1-f2|  5 MHz
Reference/Fixed
Corner Cube
Measuring/Moving
Corner Cube
Sr
Sm
Laser He-Ne
Zeeman Splitted
GCBS
(Glan Cube Beam Splitter)
Iph,r
PDr
State of Laser Polarization
f1
f2
f1
f2
PDm
Iph,m
λ/4 waveplate:
fast or slow axis at 45°
Polarizers at 45°
5 % BS
B

## Slide 19: Double-Frequency Interferometer (II)
Signals:
Iph,r = 5/100 I0 {1 + cos[2π(f1-f2)t + ]}
Iph,m = 95/100 I0 {1 + cos[2π(f1-f2)t + 2ksm - 2ksr + ]} =
  = 95/100 I0 {1 + cos[2π(f1-f2)t + 2ksm + t]}
I0 = 1/2  PL , where  is the spectral responsivity and PL is the total optical power emitted by the He-Ne (PL = 2P1 = 2P2)
Reference/Fixed
Corner Cube
Measuring/Moving
Corner Cube
Sr
Sm
Laser He-Ne
Zeeman Splitted
GCBS
(Glan Cube Beam Splitter)
Iph,r
PDr
State of Laser Polarization
f1
f2
f1
f2
PDm
Iph,m
λ/4 waveplate:
fast or slow axis at 45°
Polarizers at 45°
5 % BS
B

## Slide 20: Double-Frequency Interferometer (III)
How can we measure m = 2ksm?
Analog approach: mixing of Iph,r e Iph,m + low pass filtering to obtain cos[…] and sin[…] = DOUBLE-BEAM INTERFEROMETER!
Digital approach: digital counting of the zero-level crossing with positive or negative slope of Iph,r e Iph,m. In this way we really take advantage of the fact that now we are not performing a baseband measurement anymore!
Reference/Fixed
Corner Cube
Measuring/Moving
Corner Cube
Sr
Sm
Laser He-Ne
Zeeman Splitted
GCBS
(Glan Cube Beam Splitter)
Iph,r
PDr
State of Laser Polarization
f1
f2
f1
f2
PDm
Iph,m
λ/4 waveplate:
fast or slow axis at 45°
Polarizers at 45°
5 % BS
B

## Slide 21: Double-Frequency Interferometer (IV)
The digital counter behave like an integrator, and if we recall the fact that the frequency is defined as f = (1/2π) dφ/dt, we obtain:
CR =  [0,T] (f1-f2)dt = (f1-f2)T
CM =  [0,T] [ (f1-f2) + (2k/2)dsm/dt ]dt =  [0,T] [(f1-f2) + 2vm/]dt =
= (f1-f2)T + 2sm/, con vm = dsm/dt
T is the refresh time of the measurement

## Slide 22: Double-Frequency Interferometer (V)
The output of the subtractor is S = Cm - Cr = 2sm/ (sm = total displacement of the target in time T)
Resolution s = /2 (or /4 if we…)
What is the maximum allowed velocity for the moving target? This value is limited by the value of the carrier frequency f1-f2  5 MHz  vmax = (/2)B = 0.3 m/s (B = 1 MHz)

## Slide 23: Double-Frequency Interferometer (VI)
Pros of the two frequencies interferometer:
  Threshold value of the comparator can be set to zero, after a high pass filtering of IphR e IphM, without any loss of information
  EMI rejection is better when we work around 5 MHz
  Monitoring IphR e IphM, we can immediately stop the measure if the measuring beam is interrupted because IphR is always at 5 MHz, but IphM becomes a DC signal!

## Slide 24: Double-Frequency Interferometer (VII)
We can dramatically increase the resolution of the measurement if we mix the signals with a local oscillator fLO = (f1-f2) - fIF, con fIF = 10-100 kHz. Everything remains unchanged as the interferometric phase information is completely transferred on the carrier fIF without errors
Resolutions up to /200 can be easily achieved
time
I =
cos 2

(f - f ) t
ph,r
1
2
ph,m
I =
cos 2

(f - f ) t + 2ks
1
2
ph,m
I
I
ph,r
local oscillator
cos 2

(f -f +f ) t
IF
2
1
cos(2

f t+2ks)
cos(2

f t)
IF
IF
START
STOP
ANALOG OUT
DIGITAL COUNTS
CLOCK
at 100 f
IF
downcorverted at f
IF
f -f
1
2
:100
DIVIDER
100 f
IF
clock at
IF
f
MIXERS

## Slide 25: Hewlett Packard 5525 “THE” Laser Interferometer
Cost: about 30k€

## Slide 26: Three-Axis Version of the Interferometer
Sr
Sm
Laser He-Ne
Zeeman Splitted
Iph,r
PDr
PDm
Iph,mX
Sr
Sm
Iph,mY
Sr
Sm
Iph,mZ
FDm
FDm
BS, T = 33%
BS, T = 50%
mirror

## Slide 27: Planarity Measurement
When  is different from 0°, we find an optical path variation of 2L in the upper arm of the interferometer
Resolution of the measurement when we perform a digital measure:
  Δs = λ/2  Δ = λ/4L = 1.610-6 r = 0.32 arc-sec per L = 0.1 m
  Δs = λ/4  Δ = λ/8L = 0.810-6 r = 0.16 arc-sec per L = 0.1 m

## Slide 28: Angle Measurement