## Slide 1: “Optical Measurements” Master Degree in Engineering Automation-, Electronics-, Physics-, Telecommunication- Engineering
<number>/45
Stability Measurements and Active Stabilization of Laser Oscillator Laser Spectroscopy and Optical Frequency Metrology Prof. Cesare Svelto Politecnico di Milano
Notes: 07/29/26
<number>
Buongiorno a tutti,
sono Cesare Svelto
del Politecnico di Milano.
Questa mattina vi parlerò delle sorgenti laser in continua e delle pricipali misure per la loro caratterizzazione.
Descriveremo la struttura dei laser a stato solido e dei laser a semoconduttore (diodi laser)
per la caratterizzazione di sorgenti laser in continua e dei campioni ottici di frequenza.
La prima parte del mio intervento sarà seguita da una lezione del Prof. Elio Bava sui modelli descrittivi dell’instabilità di frequenza e sulle relative tecniche di misura.
Nella seconda metà della mia presentazione descriverò, dal punto di vista sperimentale, alcuni metodi ed esperienze di stabilizzazione e la realizzazione di campioni ottici di frequenza.

## Slide 2: Summary
<number>/45
Amplitude noise: measurement and suppression
  Technical noise, drift, and relaxation oscillation
  Feedback systems for the RIN suppression
Frequency stability and its characterization
  Causes for optical frequency instability
  Measurements with optical frequency discriminator
  The Allan variance
Laser spectroscopy
Optical frequency references and active stabilization
  Fabry-Perot discriminators and atomic/molecular references
  Fringe-Side Locking and the Pound-Drever method
Atomic/molecular optical frequency references
  Measurements on the closed-loop error signal
  or on the beat-note signal
  References at 1.5 m for the optical communications
Metrology experiments at the optical frequencies
Notes: 07/29/26
<number>
Nella seconda parte,
parleremo della soppressione del rumore d’ampiezza e ci sofferemo più in dettaglio su metodi ed esperimenti per la soppressione del rumore di frequenza.
Quindi vedremo come con un laser stabilizzato in frequenza, e opportunamente caratterizzato, sia possibile stabilire accurati campioni di frequenza ottica.
In particolare, faremo un punto della situazione sullo stato dell’arte dei riferimenti di frequenza a 1.5um per le comunucazioni ottiche.
Infine, tireremo le conclusioni sull’argomento esposto.

## Slide 3: Amplitude stability
<number>/45
Time-variable electric field with amplitude fluctuations
with a(t) << 1
Need for stabilization systems (passive/active)
( x = P/Pth )
From a perturbative analysis of the laser system (in response to small fluctuations of the pump rate or intracavity losses) we can point out the phenomenon of relaxation oscillations
  oscillation frequency
  decay time (exponential)
Notes: 07/29/26
<number>

## Slide 4: Relative Intensity Noise (RIN)
<number>/45
P
t
P(0)
P(t)
drift P(t)=P(0)-t
technical noise Prms
Spectral density SP(f)
Relative Intensity Noise
RIN(f)= SP(f) / < P >2  1Hz [dB]
Power fluctiations P(t)
RIN  Prms / Pave
Pb. 2 compl. conj. poles
often stated in dB/Hz to indicate "@1Hz" or “within a 1 Hz bandwidth"
RIN(f) =
Notes: 07/29/26
<number>

## Slide 5: RIN Suppression
<number>/45
Laser KIP
AMP
VI
BS
(1-)P
servo
PD
P
+
+
Suppl. I
Optoelectronic control loop (bandwidth and stability)
Gloop = KIP    PD · GIV  GServo  GVI
[1] = [W/A]  [1]  [A/W]· [V/A]  [V/V]  [A/V]
Notes: 07/29/26
<number>

## Slide 6: Frequency stability
<number>/45
Time-variable electric field with frequency fluctuations
inst(t)=1/(2) dtot/dt=0-(1/2) d/dt=0+ (t)
Need for stabilization systems (passive/active)
with 1/(2)  d/dt << 0
Thermal expansion coefficient: =(L/L)1/T "(...)10-6 K-1"
Al (24); steel (12); ord. glass (9); pyrex (4); INVAR (1.6); FS (0.6), ULE 0±0.0001
Strong dependence of the laser frequency from L
  e.g. for an Nd:YAG laser (=1.064 m,  300 THz)
  with L=30 cm if L=-1 m, one gets  =1 GHz!!!
  e.g. laser diode (=1.55 m,  200 THz)
  with L=500 m if L=-0.1 nm, one gets  =40 MHz!!!
From the equation of the resonator auto-frequencies:
Notes: 07/29/26
<number>

## Slide 7
<number>/45
Laser intrinsically stable monolithic laser -chip or NPRO Nd(/Tm):YAG
Diode-pumped "monolithic“ lasers are intrinsically very insensitive to perturbations destabilizing for P and 
Nd:YAG single-frequency Non-Planar Ring Oscillator
=1064 nm; P=10mW-2W; =282THz; <5kHz@1ms
Tm:YAG laser (3-levels) the active medium must be “all" inverted
PZT transducer
Peltier cell
microchip laser
PUMP
Unidirectional: spatial hole burning...
L
Notes: 07/29/26
<number>

## Slide 8
<number>/45
Frequency noise characterization (Fabry-Perot discriminator)
Airy transmission profile of a Fabry-Perot
the optical frequency fluctuations  are converted into photo-voltage fluctuations V (very important the different “gains” slope  responsivity  transimpedance gain found in the discrimination chain)
A PD can not “see” ...
fdt,ottV = fdt,ottP,ott  fdtP,ottI  fdtIV
V
interferometer
f
dt
=
f

/P
[W/Hz]
G
I-V
=
G
I-V
I
o
P
source
LASER
opt
opt

Fabry-Perot
source
LASER
voltage signal fluctuations
optical frequency fluctuations
OPTICAL FREQUENCY DISCIMINATOR trans.f. = fF/V[V/Hz]
Notes: 07/29/26
<number>

## Slide 9
<number>/45
Frequency noise characterization (optical beat-note signal)
fbeat =  fref - fopt 
if foptfopt+fopt

fbeat=fAOM-fopt
if then freffref+fref

fbeat=fAOM+fopt+fref beat-note in AC!!!
take freffopt
Sum of 2 variances of 2 independent random variables
without the (AOM)... fbatt is in DC!!!
< fref2 >1/2 << < fott2 >1/2  <( fref - fott )2 >1/2  < fott2 >1/2
< fref2 >1/2  < fott2 >1/2  < ( fref - fott)2 >1/2  < fott2 >1/2
M
fbeat=fAOM+fopt-ref
fbatt= (fref+fAOM) - fott
Spectrum Analyzer
Oscilloscope
f/V converter
Notes: 07/29/26
<number>

## Slide 10
<number>/45
Frequency noise characterization (definition of the Allan variance)
The Allan variance is the recommended measurement by several international committees and in particular by CCIR to characterize frequency stability of an oscillator in the time domain. In the case of high frequency oscillators, the Allan variance measurement, is based on the analysis of beatnote signal between two oscillators. In the case of laser sources this technique consists in taking a measurement of different samples of average beat frequency Mfbatt in adjacent time intervals and calculating the “two sample” variance between adjacent pairs. The instrument usually performing Allan variance measurements is a specific electronic counter but calculation can be performed also by PC on a time series of digitized readings of differetn values of Mfbatt,j evenly spaced by time intervals  one from the other. Having a series of N samples of the beat frequency [ Mfbatt,1, Mfbatt,2, ..., Mfbatt,N ], the Allan variance is evaluated as the average of the squares of differences between adjacent frequency samples (normalized to the squared working/mean frequency).
CCIR = Consultative Committee for International Radio
relative frequency fluctuation
y is a function of averaging time 
Notes: 07/29/26
<number>

## Slide 11
<number>/45
Frequency noise characterization (Allan variance measurement)
The two stabilized lasers have the same nominal or center frequency and hence we use an acousto-optical modulator to RF shift the beatnote frequency
“weak” frequency locking between the two lasers
M
V@ 40MHz
Verr
electronic
counter
Notes: 07/29/26
<number>

## Slide 12
<number>/45
Spectroscopy
Atoms and molecules absorption lines
Linear, FM, and saturated spectroscopy
Frequency stabilization
  fringe-side locking
  Pound-Drever
Optical frequency Metrology
  recommended wavelengths (most accurate values)
  experiments with stabilized lasers
  “optical” Atomic Clock
  second, meter, and accuracy in Measurements
Notes: 07/29/26
<number>

## Slide 13
<number>/45
Absorption lines in atoms and molecules
Atoms and molecules have an internal structure allowing electrons to have pre-defined and discrete energy levels Atoms can change from one to another energy state by absorption or emission of the required energy difference. Such energy leaps are "quantum steps" as:
E = E2-E1 = h21 = hc/21
The electromagnetic radiation of wavelength  ( frequency = c/) interacting with an atom/molecule will be more or less absorbed as a function of how much the wavelength is close to the nominal (central) transition value
0 = c/0  c /21 = hc/E = 21
Notes: 07/29/26
<number>

## Slide 14
<number>/45
Absorption lines: broadening reasons and types
When dealing with “real atoms always perturbed”, not just a single wavelength  excites the transition (giving absorption), since the spectral absorption line undergoes different causes of shift and broadening:
The absorption spectrum is in general a broadened line with central value 0 and linewidth 0,FWHM depending on the different shifts and broadening mechanisms (Voigt profile: convolution of Lorentzian and Gaussian)
physical limit due to finite lifetime of the transition: natural broadening: Lorentzian  1 / sp
external fields (e.g. Stark effect due to e.m. field from other atoms/ions) cause several shifts of line centers and hence an homogeneous broadening: Lorentzian; - collisions between atoms/molecules:
collisional broadening: Lorentzian (  p ); - velocity of the absorbers:
Doppler broading: Gaussian (  );
Notes: 07/29/26
<number>

## Slide 15
<number>/45
Absorption lines in atoms
and molecules (figures)
Molecules
Atoms
Semiconductors
C2H2
CH3D [10 kPa] R(6,3) line at  =1.543.78 nm
Notes: 07/29/26
<number>

## Slide 16
<number>/45
Absorption lines of CH3D Doppler and collisional broadenings
Doppler: gauss=
REGR. CALC. MEAS.
 1.2
Notes: 07/29/26
<number>

## Slide 17
<number>/45
Linear (direct) spectroscopy
TRANSMISSION:
If the laser, during the frequency scan, undergoes amplitude/power variations, it is convenient to normalize the power transmitted trough the cell to the emitted laser power: in fact, cell transmission is T=Pout /Pin, as a ratio of output to input powers
PD1
PD2
LASER
GAS
CELL
÷
V  T ()
We perform a linear (ramp) frequency scan of  laser and we measure the spectral profile T()
BS
M
Pin
Pout
 Pin
Notes: 07/29/26
<number>

## Slide 18
<number>/45
FM spectroscopy
During the “linear” frequency scan the laser is sine phase/frequency modulated (FM modulation). When crossing the intensity profile, the FM modulation is transformed into AM modulation.
The depth of AM modulation I() depends on the slope of the transmission curve in the working point of the spectral profile
We get the so called DISPERSION PROFILE
or “first derivative“ signal
I() out of phase 180° respect to 
I() in phase with 
I

I

Notes: 07/29/26
<number>

## Slide 19
<number>/45
FM spectroscopy experiments
Direct transmission of the cell will exhibit power ups and downs when the optical frequency is scanned trough the absorption lines
To detect absorptions smaller than 1% we use the technique of FM modulation and coherent detection (lock-in) after the cell
REF
T=1-exp(-L)
A=exp(-L)
=ln(1-T)/L
T() is obtained by integration of the "S curve" (1st derivative)
Notes: 07/29/26
<number>

## Slide 20
<number>/45
Doppler effect in spectroscopy
Number of atoms in the fundamental state (left) and excited state (right) when varying the velocity component parallel to direction (k) of the optical beam: the interaction (absorption) happens at a frequency which is shifted with respect to the center of the transition: /= v// /c
single beam
double beam counter-propagating
1 “hole“
absorption profile
symmetric double-hole
Notes: 07/29/26
<number>

## Slide 21
<number>/45
Linear vs. saturated spectroscopy
A first laser beam (powerful: pump) saturates the absorption line and a second beam (less powerful: probe) sense the saturated line
Absorbers population decreases (and hence absorption as well) at the pump laser frequency “seen" by the moving molecules (with a velocity component along the cell axis).
Double-beam interaction with the same molecules at v=0 m/s eliminates Doppler broadening and gives a much narrower saturated line [figure b)]
Notes: 07/29/26
<number>

## Slide 22
<number>/45
Saturated Spectroscopy (Doppler-free)
D atom
In Deuterium at 50 K the saturated line is not much narrower than the Doppler line. In C2H2 at 1.55 m (T=Tamb.) we have a Doppler linewidth of about 500 MHz to a saturated linewidth of 1 MHz
The pump beam is modulated (e.g. by chopper) to allow for AC detection (much more "sensitive") of the saturated line transmission profile
Notes: 07/29/26
<number>

## Slide 23
<number>/45
Stabilization
Atoms and molecules absorption lines
Linear, FM, and saturated spectroscopy
Frequency stabilization
  fringe-side locking
  Pound-Drever
Optical frequency Metrology
  recommended wavelengths (most accurate values)
  experiments with stabilized lasers
  “optical” Atomic Clock
  second, meter, and accuracy in Measurements
Notes: 07/29/26
<number>

## Slide 24
<number>/45
Frequency Stabilization ( general principle scheme )
LASER
Notes: 07/29/26
<number>

## Slide 25
<number>/45
Frequency Stabilization ( fringe-side locking method )
V is the error signal
(ratio or difference)
 frequency signal f=-*
with ”moderate” locking
Notes: 07/29/26
<number>

## Slide 26
<number>/45
Frequency Stabilization ( Pound-Drever method )
modulation phase/frequency 
addition of “two” side bands
interrogation of dispersion (phase) profile 
different phase shifts 
unbalance of lock-in detected signal 
error signal (“odd“ simetry vs. detuning)
C2H2
0200THz
Notes: 07/29/26
<number>

## Slide 27
<number>/45
Frequency Stabilization ( Pound-Drever method – EQUATIONS )
we get two optical beat signals at the modulation frequency fm=/2m/2: a first one between carrier (at frequency =/2) and left sideband and a first one between carrier and left sideband
(without the optical resonance sidebands J1 and J-1 beating with carrier J0 do not produce any amplitude modulation at frequency fm, as correct for a pure FM)
When the phase-modulated optical field senses the resonance,
Optical electric field phase modulated (sine mod.):
or m is the angular frequency of phase modulation  is the modulation depth
Notes: 07/29/26
<number>

## Slide 28
<number>/45
Frequency Stabilization ( Pound-Drever method – DISCRIMINATION )
When the optical carrier is at the line center, amplitudes of the two beat signals are equal but with opposite phases: the resulting amplitude at frequency fm is null
When the optical carrier is shifted from line center, amplitudes of the two beat signal are still almost equal but the two phases, (Φ0–Φ-1) and (Φ0-Φ1), differ by a quantity 2Φ0, beeing still Φ1-Φ-1 but now Φ0 0, and hence the resulting amplitude at frequency fm is proportional to sin(2Φ0)(2Φ0)=(-0)
 error signal  frequency detuning (with sign!)
Φ0=(-0)
Notes: 07/29/26
<number>

## Slide 29
<number>/45
Metrology
Atoms and molecules absorption lines
Linear, FM, and saturated spectroscopy
Frequency stabilization
  fringe-side locking
  Pound-Drever
Optical frequency Metrology
  recommended wavelengths (most accurate values)
  experiments with stabilized lasers
  “optical” Atomic Clock
  second, meter, and accuracy in Measurements
Notes: 07/29/26
<number>

## Slide 30: Metrologia alle frequenze ottiche: lunghezze d’onda “raccomandate”
<number>/45
12 lunghezze d’onda “ottiche” raccomandate, dal CIPM (1997) e da lavori del CCL, per la realizzazione del "metro“ (def. 1983)
2 note con accuratezza 10-12
3 note con accuratezza 10-11
nel 2003 le  diventano 13 e le accuratezze migliorano...
Notes: 07/29/26
<number>

## Slide 31: Optical Frequency Metrology: “most accurate” wavelengths
<number>/45
in 2007 recommended  became 20 with accuracy up to 310-15
Absorbing ion 199Hg+, 5d106s 2S1/2 (F = 0) – 5d96s2 2D5/2 (F = 2) ∆mF=0
CIPM recommended values
  f = 1 064 721 609 899 145 Hz (1000 THz)
  λ = 281 568 867.591 968 6 fm (280 nm)
with a relative standard uncertainty of 3 × 10−15, apply to the
unperturbed quadrupole transition of a trapped and cooled mercury ion
88Sr+ uncertainty of 7×10−15 ; 171Yb+ uncertainty of 9×10−15
40Ca uncertainty of 1.8×10−14 ; OsO4 uncertainty of 1.4×10−13
1H uncertainty of 2.0×10−13 ; 115In+ uncertainty of 3.6×10−13
127I2 uncertainty of 8.9×10−12 ; 13C2H2 uncertainty of 2.6×10−11
Notes: 07/29/26
<number>

## Slide 32: Experiments with Nd:YAG Lasers freq. doubled and stabilizd to I2
<number>/45
f -2
f -1
G. Galzerano, C. Svelto, E. Bava, F. Bertinetto, Appl. Opt. (1999)
J. Hall, ... (2000)
Nobel Prize!!! (2005)
Notes: 07/29/26
<number>

## Slide 33: The Acetylene Molecule (C2H2) and Stabilized Er-Yb Lasers
<number>/45
50 resolved lines
spaced by 100GHz
and large 0.5GHz
p=1kPa, L=10cm
slope=0.4mV/MHz
rms=160kHz<10-9
Analysis of beat-note frequency
riga P(15)
01534 nm
0195 THz
Notes: 07/29/26
<number>

## Slide 34: International Experiments at 1.5 m
<number>/45
2-photon Rb (=778nm)
(laser=1.556m)
stability = 2kHz (10-11)
accuracy = 20kHz
saturated 13C2H2 (=1550.18nm)
(laser=1.55m)
stability = 2kHz (10-11)
accuracy = 200kHz
A. Onae et al.
Notes: 07/29/26
<number>

## Slide 35: Experiments PoliMI et al. at 1.5 m
<number>/45
freq. stab. /10-12
Notes: 07/29/26
<number>

## Slide 36: Experiments PoliMI et al. at 1.5 m
<number>/45
Transmission (offset) [1]
freq. stab. /210-12
Notes: 07/29/26
<number>

## Slide 37: Optical Atomic Clock - single Sr+ ion (yr. 2002)
<number>/45
9 GHz
Atomic clock
by 133Cs
SI “second”
445 THz
(674 nm)
Canada
Q  1015
Notes: 07/29/26
<number>

## Slide 38: Optical Atomic Clock - Sr+ multi-ion (1/3)
<number>/45
http://www.newscientist.com/ New Scientist Breaking News
The most accurate clock of all time
18:00 18 May 2005
Related Articles
13 July 2001 World's most accurate clock created
 Max Plank Institute for Quantum Optics
 Department of Quantum Engineering and Systems Science, University of Tokyo
If “TIME waits for no man”, then neither does human ingenuity in measuring its passing. Throughout history, more stable and accurate clocks have led to advances in communications and navigation. Now a clock 1000 times more accurate than any of its predecessors has set another benchmark, and could even be used to create a more precise definition of how long a second is. The new clock is a variant on the atomic clocks that appeared in the 1950s. Atomic clocks usually work by measuring the frequency at which atoms resonate. For instance, the outer electrons of a caesium-133 atom resonate between two energy states exactly 9,192,631,770 times each second, emitting microwaves of exactly that frequency as they do so. This property has been used since 1967 to define what we mean by 1 second - it is officially the time it takes for a caesium atom to resonate 9,192,631,770 times.
Notes: 07/29/26
<number>

## Slide 39
<number>/45
“One way to create a more accurate clock is to increase the rate at which it ticks”. The first atomic clocks could pin this down to an accuracy of 1 part in 1010.
Today's caesium clocks can measure time to an accuracy of 1 in 1015, or 1 second in about 30 million years. But the search is on for ever more precise timepieces.
"A clock has a counter that counts something that is periodic. The shorter that period is, the more accurate the clock. That is why people went from sundials, with one period per day, to pendulum clocks, with one period per second, to quartz clocks with 10,000 oscillations per second. Now we have the caesium clock counting with 9 billion oscillations per second.“
So what ticks faster than a caesium atom? Elements being scrutinized include ytterbium, mercury and strontium (which resonates 429,228,004,229,952 times each second). But until now it has proved impossible to create a useful strontium atomic clock. In principle, there are two ways to create a strontium clock: using the oscillations of a single atom, or doing the same with many atoms at the same time.
The advantage of using a single atom is that it is relatively easy to shield it from external electromagnetic fields, which interfere with its oscillating frequency. The disadvantage is that it is extremely difficult to accurately measure a single atom vibrating at such a high frequency. A multi-atom clock produces a much clearer signal but is less accurate, because the electromagnetic fields of the atoms interfere with each other.
Optical Atomic Clock - Sr+ multi-ion (2/3)
Notes: 07/29/26
<number>

## Slide 40
<number>/45
Now Hidetoshi Katori and his colleagues at the University of Tokyo have come up with an elegant solution that combines the advantages of both systems (Nature, vol 435, p 321). Katori uses six laser beams to create a pattern of standing electromagnetic waves. This creates a series of energy wells, each of which supports one strontium atom, in much the same way as each dimple in an egg box holds an egg (see Diagram). This prevents the electromagnetic fields of individual atoms interfering with those of their neighbors, and allows the oscillating signals of many atoms to be measured at once. Previous attempts to make clocks this way failed because the trapping lasers themselves interfered with the atoms' oscillation frequency.
Katori‘s group has got round this by tuning the frequencies of the lasers so they alter the upper and lower transition energy levels of strontium by exactly the same amount, so the oscillation frequency remains unaltered. Katori claims that this "optical lattice clock" will keep time with an accuracy of 1 part in 1018.
 430 THz
 700 nm
Optical Atomic Clock - Sr+ multi-ion (3/3)
Notes: 07/29/26
<number>

## Slide 41: Optical Atomic Clock - single Yb+ ion
<number>/45
=467nm
=642THz
1nHz
Q=/ 61023
( NPL UK )
Notes: 07/29/26
<number>

## Slide 42: Optical Spectroscopy and the “SI meter"
<number>/45
High-resolution spectroscopy of atoms and molecules has been, and continues to be an essential experimental tool in the formulation and development of quantum
mechanics, the measurement of atomic properties, the determination of fundamental
constants, and in the realization of standards for time and length. Not only are we
able to directly probe the detailed structure of atoms and molecules but also test the
invariance of the velocity of light as postulated by the theory of special relativity,
which has allowed us to redefine the SI unit of length and realize it in terms of
experimental observables of quantized systems rather than physical artifacts.
The SI unit of length was originally intended to be one ten millionth part of the
quadrant of the Earth, and the original 1799 metre was based on measurements made
along a meridian from Dunkerque to Barcelona represented an attempt to realize this
length. Such a physical artifact remained in the definition of the metre until 1960
when the definition was replaced by one based on a measurement of the wavelength
of orange light emitted by excited atoms of an isotope of krypton. This definition was eventually superseded in 1983 by the present one, which is derived by assigning a defined value to the speed of light in free space. Today, the SI unit of the metre is
‘the length of the path traveled by light in vacuum during a time interval of
1/299 792 458 of a second’, thus fixing the velocity of light at 299 792 458 m s–1.
Notes: 07/29/26
<number>

## Slide 43: Accuracy Limits in MEASUREMENTS
<number>/45
With a fixed velocity of light relating distance and time, and hence frequency and
wavelength, the ability to measure time more accurately than other physical quantities
provides a much improved realization of the metre. In principle, we are limited only by the accuracy of the time reference.
At present the best microwave time standard based on transitions within caesium atoms has an accuracy of about one part in 1015,
whereas the best optical frequency standards (spectroscopy of laser cooled single atoms and ions) are expected to approach a level of one part in 1018.
The developments in optical comb technology represented by the measurements of
Long-Sheng Ma et al. (a collaboration involving the Bureau International des Poids et
Mesures, Sèvres, France; Physics Department, East China Normal University,
Shanghai, China; National Institute of Standards and Technology, Boulder, CO, USA;
and OFS Laboratories, Murray Hill, New Jersey, USA), recently reported in Science
(19th March, 2004), demonstrate the potential to connect the frequency of radiation in the optical range of the electromagnetic spectrum to the frequency of radiation in the radiofrequency domain with an accuracy approaching one part in 1019.
Notes: 07/29/26
<number>

## Slide 44: Bibliography
<number>/45
M. Ohtsu, Frequency Control of Semiconductor Lasers, Wiley, New York, 1996
R.W.P. Drever, J.L. Hall, F.V.Kowalsky, J. Hough, G.M. Ford, A. J. Munley, and H. Ward, Laser Phase and frequency stabilization using an optical resonator, Appl. Phys. B 31, 97-105, 1983
C. Svelto, G. Galzerano, Frequency-Stabilized Near-Infrared Solid-State Lasers, Recent Research Developments in Applied Physics, 2001
http://www.bipm.fr/en/scientific/length/international_comparisons.html
T. J. Quinn, Practical realization of the definition of the metre, including recommended radiations of other optical frequency standards (2001), Metrologia 40,103–133, 2003
Notes: 07/29/26
<number>
Riportiamo, infine, i riferimenti ad alcuni testi scientifici che possono essere usati per approfondimenti sugli argomenti presentati.
E’ stato un privilegio e un piacere insegnare in questa Scuola.
Gazie per la vostra attenzione.

## Slide 45: Bibliography
<number>/45
https://en.wikipedia.org/wiki/Frequency_comb
http://www2.mpq.mpg.de/~haensch/comb/
Theodor W. Hänsch, PASSION FOR PRECISION, Nobel Lecture, December 8, 2005
Jun Ye and Steven T. Cundiff, Femtosecond Optical Frequency Comb: Principle, Operation, and Applications, Kluwer Academic Publishers / Springer Norwell, MA, 2005
John Hall and Theodor W. Hänsch, Optical frequency combs and frequency comb spectroscopy, TULIP Summer School IV 2009, Noordwijk, April 15-18
Notes: 07/29/26
<number>
Riportiamo, infine, i riferimenti ad alcuni testi scientifici che possono essere usati per approfondimenti sugli argomenti presentati.
E’ stato un privilegio e un piacere insegnare in questa Scuola.
Gazie per la vostra attenzione.