## Slide 1
<number>/33
Electro-optical
Instrumentation
by S. Donati
University of Pavia, Italy
+additions
(C. Svelto)

## Slide 2
<number>/33
Electro-optical Instrumentation starts to appear in the‘70, soon after the laser is developed.
Big successes like telemeters, gyroscopes, laser interferometers, laser velocimeters, particle size analyzers - are just few examples of instruments that have marked milestones in the science of measurement and gained general acceptance in engineering applications.
ELECTRO-OPTICAL INSTRUMENTATION

## Slide 3
<number>/33
Improvements and new concepts continue to boost R&D activity and promote the growth of a wealthy market of E-O instruments.
Electro-optical instruments are products
spreading from industry and manufacturing to scientific applications, from avionics and space to medicine and biology.
ELECTRO-OPTICAL INSTRUMENTATION

## Slide 4
<number>/33
Despite a market smaller than fiberoptic telecommunication, electro-optical instrumentation is steadily increasing from year to year, and is immune to bubble-economy effects.
ELECTRO-OPTICAL INSTRUMENTATION
W
o
r
l
d
M
a
r
k
e
t
o
f
O
p
t
i
c
a
l
F
i
b
e
r
C
o
m
m
u
n
i
c
a
t
i
o
n
s
(
c
o
m
p
o
n
e
n
t
s
a
n
d
s
y
s
t
e
m
s
)
:
3
5
0
0
0
M
$
(
1
9
9
8
)
4
4
0
0
0
(
1
9
9
9
)
4
0
0
0
0
(
2
0
0
0
)
1
0
0
0
0
(
2
0
0
2
)
W
o
r
l
d
M
a
r
k
e
t
o
f
E
l
e
c
t
r
o
-
O
p
t
i
c
a
l
I
n
s
t
r
u
m
e
n
t
a
t
i
o
n
(
y
e
a
r
2
0
0
0
)
c
i
v
i
l
2
3
0
0
M
$
a
v
i
o
n
i
c
s
3
4
0
0
m
i
l
i
t
a
r
y
2
8
0
0
t
o
t
a
l
8
5
0
0
M
$
(
a
n
n
u
a
l
g
r
o
w
t
h
+
6
%
,
L
a
s
e
r
F
o
c
u
s
e
s
t
i
m
a
t
e
)

## Slide 5
<number>/33

## Slide 6
<number>/33
ELECTRO-OPTICAL INSTRUMENTATION
telemetry
The album of successes:
interferometry
gyroscopes
velocimetry
Notes: <number>

## Slide 7
<number>/33
TELEMETRY
Telemetry started with LURE (LUnar Ranging Experiment), an experiment carried out in 1970 when the astronauts of Apollo 11 brought on the moon an array of corner-cubes (100 x 1” dia.). Five telescopes on earth aimed the array with their Q-switched ruby lasers, launching a 0.5-J, 10-ns pulse. Three telescopes got the return, a ≈ 10-photon pulse. The time-of-flight measurement translated into a distance measured with an accuracy ≈ 30 cm for the 384 000 km distance.
Ppeak = ?
Eriv,red = ?
50 MW!!!
10h=10hc/=3 aJ
0.5 J  3 aJ  A1019
0.3m/4108m=0.7510-91ppb!!!
tA1.3 s e tA-R2.6 s
Err(L)=0.3 m  Err(t )=1 ns

## Slide 8
<number>/33
TELEMETRY
In 1999, the MOLA (Mars-Orbiter Laser-Altimeter) of the Pathfinder
mission has completed a 2-year survey of the topography with 5-m
height resolution on 100x100-m2 individual areas covering Mars
Fake-colors altimetric map of the surface of planet Mars

## Slide 9
<number>/33
TELEMETRY
TAV 34
télémètre aéroporté à laser (CILAS (1969)
Meanwhile,
telemeters
were deployed in avionics
(RANGEFIN-DERS)
and. . .

## Slide 10
<number>/33
TELEMETRY
. . in civil-
-engineering applications:
TOPOGRAPHY
they marked the retirement
of the
theodolite

## Slide 11
<number>/33
TELEMETRY
. . .and they originated the
LIDAR,
for air pollution monitoring

## Slide 12
<number>/33
TELEMETRY
. . . as well as in
the automotive
to become an anti-collision
system
and a key
subsystem for automated driver of next decade

## Slide 13
<number>/33
In adaptive cruise control, anti-collision telemeter and vision system are coupled to side-detection sensors to improve safety. Next step will be the automated driver
(from: Spectrum IEEE, Jan. 2000)
AUTOMATED DRIVER
Sogno... ancora futuribile
  

## Slide 14
<number>/33
INTERFEROMETRY
A well-known technique (used in optics since the 1800s),
now exploiting the long coherence length of lasers
The first ‘laser interferometer’ appears in 1965 (HP5526)
since then, 2K .. 5K units sold per year (a big success!)
The first scientific experiments (1968): earth crust tides
Doppler velocimeters follow in 1970s (another success!)
ElectronicSpecklePatternInterferometry vibration/strain analyzers in 1975
widespread applications, a big tree growing up . . .

## Slide 15
<number>/33
INTERFEROMETERS
Interferometry is a big tree with roots in optics, electronics, e.m. fields, measurement science, and technology.
It is since the advent of the laser that it has grown out in so many new branches

## Slide 16
<number>/33
INTERFEROMETERS
The Laser Interferometer HP5525, since its inception has established a new standard of machine-tool measurement. It can ensure a 0.1 m resolution and accuracy to displacement measurements up to several meter range

## Slide 17
<number>/33
INTERFEROMETERS
Progresses in recent years have extended the interferometric resolution to the image format, creating a new tool for inspection and diagnostics (Wyko 2000).
LASER profilometer

## Slide 18
<number>/33
INTERFEROMETERS: LIGO
LIGO is the Laser Interferometer Gravitational-Wave Observatory
LIGO is a joint project between scientists of the California Institute of Technology (Caltech) and Massachussetts Institute of Technology (MIT), funded by the National Science Foundation (NSF). In year 2002 it costed 365 millions of dollars, and it was the biggests and most ambitious programme ever financed by the NSF.
Gravitational waves, theoretically predicted by the Relativity general Theory by Einstein in 1916 and generated at hundreds of millions of light years from the Earth, should deform the 4 km space between two mirrors of approx. 10-18 m (the diameter of an hydrogen atom is approx. 5×10-11 m, 0.5 Ǻ).
In order to detect this tiny deformation of the space, an ultra-stable ultra-sensitive laser interferometer is needed

## Slide 19
<number>/33
INTERFEROMETERS: LIGO
Meanwhile, big science does not stop! LIGO is a gravitational
wave detector (a balanced Michelson interferometer
with 4-km arm length) actuated by 10-kg test masses suspended in vacuum
Laser Interferometer Gravitational(-wave) Observatory

## Slide 20
<number>/33
INTERFEROMETERS: LIGO
The first step, the LIGO I interferometer, is designed to attain a 10-22 m/m strain sensitivity, a record performance
210-22 m/m

## Slide 21
<number>/33
INTERFEROMETERS: LIGO
With such a sensitivity (right), LIGO I should be able to detect neutron star and supernova collapse up to 100 Mparsec – 31023 m 325 million light years – away from Earth
Spurious signals will be ruled out by a coincidence principle (below)
W
V

## Slide 22
<number>/33
INTERFEROMETERS: LISA
LISA will be able to detect the most powerful outflows of energy in the Universe, generated when two massive black holes orbit, collide, and merge. These mergers will produce gravitational waves, sometimes called "ripples in space-time."
Laser Interferometer Space Antenna

## Slide 23
<number>/33
INTERFEROMETERS: LISA
As long wavelength gravitational waves encounter LISA, they will generate small changes in the distance between the spacecrafts. We will be able to measure any changes in the armlengths down to 10 picometers (about 1/10th the size of an atom)!
L  510 9 m
(5 million km!)
10pm/5109m=210-21!!!

## Slide 24
<number>/33
GYROSCOPES
1962: shortly
after the He-Ne laser invention (1960), W. Macek experimented at Sperry the first laser gyro concept and was able to detect earth rotation (15°/h)
410-3 °/s!!!

## Slide 25
<number>/33
GYROSCOPES : the RLG
It took 12 years of engineering efforts for the RLG to become (1975) the heart of INU - Inertial Navigation Units
This 8-cm side RLG has a 0.001°/h performance
0.310-6 °/s!!!

## Slide 26
<number>/33
RLG INU
Since 1980, any new aircraft is equipped
with a 3-axis RLG INU
capable of 1 mile/hour
0.05° attitude
and 3-m heigth accuracy,
in a 603020 cm3 box tagged
at 1.8 M$ price
Litton LN-93

## Slide 27
<number>/33
Fiberoptics Gyroscope (FOG)
Meanwhile (1975) the fiber-optics-gyroscope is developed, less performing but more rugged and lightweight, now used to stabilize communication satellites . . .

## Slide 28
<number>/33
Space FOG
The Iridium World Satellite Service
. . like
in the
IRIDIUM
network of
worldwide
cellular
telephone
  

## Slide 29
<number>/33
Automotive FOG
Magneti Marelli RP
. . . and to
backup the
attitude GPS
system in
Route Planners
(or, automotive
navigation
system)
  

## Slide 30
<number>/33
LASER PARTICLE IMAGE VELOCIMETRY (Laser-PIV)
Laser light is used to “light up” small particles moving with the fluid and the images of the lit particles allow calculation of the velocity field

## Slide 31
<number>/33
LASER DOPPLER VELOCIMETRY (LDV)
Nowadays another well-established electro-optical instrument for sensing and measurements of velocity in fluids, the LDV makes non-contact measurement and covers the amazing range from ≈1 m/s to over 1 km/s

## Slide 32
<number>/33
Particle Size Measurement
In Laboratory Analysis, particle size analyzers are workhorse for testing of chemical biochemical, medical and industrial samples. Using a revolver feeder of cuvettes, assay is automated (courtesy of CILAS)
Notes: <number>
Thus, one chooses a reasonable number of diameters to get the best result. A strategy is to increase the K of diameters and repeat the calculation until in the new result oscillations or wrong features start to show up. Usually, the range of diameter of interest may be large (typ, two decades from 2 to 200m) but the number of affordable diameter is modest (e.g. K=6). Of course, the cumu-lative distribution P(D) looks more regular than the density function p(D).
Other Linear Methods. The basic LSM we have outlined above is the starting point for several extensions. A straight example is weighting of terms contributing to the total error 2, adding in the equation a multiplying factor wn that is taken =1 where the measured In is clean (or, has a good S/N ratio), and <1 where In is noisy. Of course, the choice of the exact weight is somehow arbitrary, or left to our knowledge of the powder nature.
Iterative Methods. The prototype is Chahine’s method used to invert Fredholm’s equation in a variety of applications. We start letting K=N, that is, using a number of unknown variables pk equal to the number of measured intensities In (K=N is also provided by the application of the LSM, first). Now, if the set of diameter distribution pk is correct, it should give the measured distribution In.calc= kCnkpk. If the set of calculated values In.calc differs from the experimental values, then we may expect to approach the solution by multiplying pk by Ik.meas/Ik.calc, where Ik.meas are the measured values, or explicitly: pk+1 = Ik.meas/Ik.calc pk. By repeating the procedure, pk should converge to the correct solution. The trial values of pk may be either an estimated distribution or the result of a LSM calculation. Chahine’s method is definitely better than the normal LSM. Errors are reduced by a factor ≈3..5, and the range of D’s is increased. 

## Slide 33
<number>/33
Electro-Optical Instrumentation
Classes of electro-optical instruments and the lasers they use
_____________________________________________________________________________________________
Application Typical Laser Main Characteristic
_____________________________________________________________________________________________
ALIGNMENT, POINTING He-Ne and
and TRACKING semiconductor collimation, beam quality
DIAMETER SENSOR
and PARTICLE SIZING He-Ne collimation, beam quality
TELEMETERS
- geodimeter (d >1 km) solid state (Nd, etc.) high peak-power (Q-switched)
- topograph (d <1 km) GaAs diode high-frequency modulation
INTERFEROMETERS He-Ne temporal coherence, 6-digit
for dimensional metrology (Nd:YAG 2) wavelength-accuracy
Doppler VELOCIMETERS He-Ne, Ar spatial coherence, beam quality
ESPI vibration analyzers He-Ne, Ar spatial coherence, beam quality
FOG gyroscopes and GaAlAs diode high radiance,
Fiber Optics Sensors and SLED controlled temporal coherence
Notes: <number>
Thus, one chooses a reasonable number of diameters to get the best result. A strategy is to increase the K of diameters and repeat the calculation until in the new result oscillations or wrong features start to show up. Usually, the range of diameter of interest may be large (typ, two decades from 2 to 200m) but the number of affordable diameter is modest (e.g. K=6). Of course, the cumu-lative distribution P(D) looks more regular than the density function p(D).
Other Linear Methods. The basic LSM we have outlined above is the starting point for several extensions. A straight example is weighting of terms contributing to the total error 2, adding in the equation a multiplying factor wn that is taken =1 where the measured In is clean (or, has a good S/N ratio), and <1 where In is noisy. Of course, the choice of the exact weight is somehow arbitrary, or left to our knowledge of the powder nature.
Iterative Methods. The prototype is Chahine’s method used to invert Fredholm’s equation in a variety of applications. We start letting K=N, that is, using a number of unknown variables pk equal to the number of measured intensities In (K=N is also provided by the application of the LSM, first). Now, if the set of diameter distribution pk is correct, it should give the measured distribution In.calc= kCnkpk. If the set of calculated values In.calc differs from the experimental values, then we may expect to approach the solution by multiplying pk by Ik.meas/Ik.calc, where Ik.meas are the measured values, or explicitly: pk+1 = Ik.meas/Ik.calc pk. By repeating the procedure, pk should converge to the correct solution. The trial values of pk may be either an estimated distribution or the result of a LSM calculation. Chahine’s method is definitely better than the normal LSM. Errors are reduced by a factor ≈3..5, and the range of D’s is increased. 